Internet Printing Protocol Working Group                     Pat Fleming

INTERNET DRAFT                                                       IBM

<draft-ietf-ipp-ldap-printer-schema-05.txt>                    Ken Jones

[Target Category: Informational]                                eStarCom

Expires 28 February 2002                                     Harry Lewis

IBM

Ira McDonald

High North Inc

28 August 2001

Internet Printing Protocol (IPP):

LDAP Schema for Printer Services

Copyright (C) The Internet Society (2001). All Rights Reserved.

Status of This Memo

This document is an Internet-Draft and is in full conformance with

all provisions of Section 10 of RFC 2026.  Internet-Drafts are

working documents of the Internet Engineering Task Force (IETF), its

areas, and its working groups.  Note that other groups may also

distribute working documents as Internet-Drafts.

Internet-Drafts are draft documents valid for a maximum of six months

and may be updated, replaced, or obsoleted by other documents at any

time.  It is inappropriate to use Internet-Drafts as reference

material or to cite them other than as "work in progress."

To view the list of Internet-Draft Shadow Directories, see

http://www.ietf.org/shadow.html.

Abstract

This document provides information for the Internet community.  It

does not specify an Internet standard of any kind.  This document

defines an LDAP schema, object classes and attributes, for printers

and printer services, for use with directories that support

Lightweight Directory Access Protocol (LDAPv3) [RFC2251].  This

document is based on the printer attributes listed in Appendix E of

Internet Printing Protocol (IPP/1.1) [RFC2911], the Service Location

Protocol (SLPv2) [RFC2608] 'service:printer:' template defined in

[SLPPRT], and the mapping between SLP service advertisements and LDAP

descriptions of services defined in [RFC2926].  Send comments to the

IPP WG <ipp@pwg.org> and the editor <flemingp@us.ibm.com>.

Fleming, Jones, Lewis, McDonald    Expires 28 February 2002     [Page 1]

Internet Draft      LDAP Schema for Printer Services      28 August 2001

Table of Contents

1.  Introduction ...............................................       4

2.  Terminology ................................................       4

3.  Definition of Object Classes ...............................       5

3.1.  slpServicePrinter ......................................       6

3.2.  printerAbstract ........................................       6

3.3.  printerService .........................................       7

3.4.  printerServiceAuxClass .................................       7

3.5.  printerIPP .............................................       8

3.6.  printerLPR .............................................       8

4.  Definition of Attribute Types ..............................       9

4.1.  printer-uri ............................................      10

4.2.  printer-xri-supported ..................................      11

4.3.  printer-name ...........................................      11

4.4.  printer-natural-language-configured ....................      12

4.5.  printer-location .......................................      12

4.6.  printer-info ...........................................      13

4.7.  printer-more-info ......................................      13

4.8.  printer-make-and-model .................................      13

4.9.  printer-ipp-versions-supported .........................      14

4.10.  printer-multiple-document-jobs-supported ..............      14

4.11.  printer-charset-configured ............................      14

4.12.  printer-charset-supported .............................      15

4.13.  printer-generated-natural-language-supported ..........      15

4.14.  printer-document-format-supported .....................      15

4.15.  printer-color-supported ...............................      15

4.16.  printer-compression-supported .........................      16

4.17.  printer-pages-per-minute ..............................      16

4.18.  printer-pages-per-minute-color ........................      16

4.19.  printer-finishings-supported ..........................      17

4.20.  printer-number-up-supported ...........................      17

4.21.  printer-sides-supported ...............................      17

4.22.  printer-media-supported ...............................      17

4.23.  printer-media-local-supported .........................      18

4.24.  printer-resolution-supported ..........................      18

4.25.  printer-print-quality-supported .......................      18

4.26.  printer-job-priority-supported ........................      19

4.27.  printer-copies-supported ..............................      19

4.28.  printer-job-k-octets-supported ........................      19

4.29.  printer-current-operator ..............................      20

4.30.  printer-service-person ................................      20

4.31.  printer-delivery-orientation-supported ................      20

4.32.  printer-stacking-order-supported ......................      20

4.33.  printer-output-features-supported .....................      21

4.34.  printer-aliases .......................................      21

5.  Definition of Syntaxes .....................................      22

6.  Definition of Matching Rules ...............................      22

7.  IANA Considerations ........................................      23

8.  Internationalization Considerations ........................      23

9.  Security Considerations ....................................      23

Fleming, Jones, Lewis, McDonald    Expires 28 February 2002     [Page 2]

Internet Draft      LDAP Schema for Printer Services      28 August 2001

10.  References ................................................      23

11.  Acknowledgments ...........................................      24

12.  Authors' Addresses ........................................      25

13.  Full Copyright Statement ..................................      26

Fleming, Jones, Lewis, McDonald    Expires 28 February 2002     [Page 3]

Internet Draft      LDAP Schema for Printer Services      28 August 2001

1.  Introduction

This document provides information for the Internet community.  It

does not specify an Internet standard of any kind.  This document

defines an LDAP schema, object classes and attributes, for printers

and printer services, for use with directories that support

Lightweight Directory Access Protocol (LDAPv3) [RFC2251].  This

document is based on the printer attributes listed in Appendix E of

Internet Printing Protocol (IPP/1.1) [RFC2911], the Service Location

Protocol (SLPv2) [RFC2608] 'service:printer:' template defined in

[SLPPRT], and the mapping between SLP service advertisements and LDAP

descriptions of services defined in [RFC2926].  Send comments to the

IPP WG <ipp@pwg.org> and the editor <flemingp@us.ibm.com>.

Appendix E of IPP/1.1 [RFC2911] specifies a list of printer

attributes which should be included in a general directory schema

describing IPP print services.  The syntax for each of these

attributes is described in detail in [RFC2911] and [SLPPRT].  This

document takes these attributes and maps them to LDAP attributes and

object classes.

This document defines several object classes to provide LDAP

applications with flexible options in defining printer information

using LDAP schema.  Classes are provided for defining directory

entries with common printer information and for extending existing

directory entries with SLPv2 [RFC2608], IPP/1.1 [RFC2911], and LPR

[RFC1179] specific information.

2.  Terminology

This document provides information for the Internet community.  It

does not specify an Internet standard of any kind.

For systems which choose to support this LDAP printer schema, the key

words "MUST", "MUST NOT", "REQUIRED", "SHALL", "SHALL NOT", "SHOULD",

"SHOULD NOT", "RECOMMENDED", "MAY", and "OPTIONAL" in sections 3 and

4 of this document are to be interpreted as described in [RFC2119].

Fleming, Jones, Lewis, McDonald    Expires 28 February 2002     [Page 4]

Internet Draft      LDAP Schema for Printer Services      28 August 2001

3.  Definition of Object Classes

We define the following LDAP object classes for use with both generic

printer related information and services specific to SLPv2 [RFC2608],

IPP/1.1 [RFC2911], and LPR [RFC1179].

slpServicePrinter - auxiliary class for SLP registered printers

printerAbstract - abstract class for all printer classes

printerService - structural class for printers

printerServiceAuxClass - auxiliary class for printers

printerIPP - auxiliary class for IPP printers

printerLPR - auxiliary class for LPR printers

The following are some examples of how applications MAY choose to use

these classes when creating directory entries:

1) Use printerService for directory entries containing common printer

information.

2) Use both printerService and slpServicePrinter for directory

entries containing common printer information for SLP registered

printers.

3) Use printerService, printerLPR and printerIPP for directory

entries containing common printer information for printers that

support both LPR and IPP.

4) Use printerServiceAuxClass and object classes not defined by this

document for directory entries containing common printer information.

In this example, printerServiceAuxClass is used for extending other

structural classes defining printer information with common printer

information defined in this document.

Note that specifying the abstract object class printerAbstract is

OPTIONAL when using printerService or printerServiceAuxClass to

create directory entries per [RFC2251].

Refer to Section 4 for definition of attribute types referenced by

these object classes.  We use names instead of OIDs in MUST and MAY

for clarity.  Some attribute names described in [RFC2911] have been

prefixed with 'printer-' as recommended in [SLPPRT] and [RFC2926].

For the object classes defined in this section, schema developers MAY

add to the list of MAY OIDs, but MUST NOT modify the list of MUST

OIDs and MUST NOT remove OIDs from the list of MAY OIDs.  Schema

developers MAY derive additional classes from the abstract and

structural classes defined in this section.  Note, an object class

definition SHOULD NOT be changed without having a new name and OID

assigned to it.

Fleming, Jones, Lewis, McDonald    Expires 28 February 2002     [Page 5]

Internet Draft      LDAP Schema for Printer Services      28 August 2001

3.1.  slpServicePrinter

This auxiliary class defines Service Location Protocol (SLPv2)

[RFC2608] specific information.  It MUST be used with a structural

class such as printerService.  It MAY be used to create new or extend

existing directory entries with SLP 'service:printer' abstract

service type information as defined in [SLPPRT].  This object class

is derived from 'slpService', the parent class for all SLP services,

defined in [RFC2926].

( 1.3.18.0.2.6.254

NAME  'slpServicePrinter'

DESC  'Service Location Protocol (SLP) information.'

AUXILIARY

SUP   slpService

)

3.2.  printerAbstract

This abstract class defines printer information.  It is a base class

for deriving other printer related classes, such as, but not limited

to, classes defined in this document.  It defines a common set of

printer attributes that are not specific to any one type of service,

protocol or operating system.

( 1.3.18.0.2.6.258

NAME  'printerAbstract'

DESC  'Printer related information.'

ABSTRACT

SUP   top

MAY   ( printer-name $

printer-natural-language-configured $

printer-location $ printer-info $ printer-more-info $

printer-make-and-model $

printer-multiple-document-jobs-supported $

printer-charset-configured $ printer-charset-supported $

printer-generated-natural-language-supported $

printer-document-format-supported $ printer-color-supported $

printer-compression-supported $ printer-pages-per-minute $

printer-pages-per-minute-color $

printer-finishings-supported $ printer-number-up-supported $

printer-sides-supported $ printer-media-supported $

printer-media-local-supported $

printer-resolution-supported $

printer-print-quality-supported $

printer-job-priority-supported $ printer-copies-supported $

printer-job-k-octets-supported $ printer-current-operator $

Fleming, Jones, Lewis, McDonald    Expires 28 February 2002     [Page 6]

Internet Draft      LDAP Schema for Printer Services      28 August 2001

printer-service-person $

printer-delivery-orientation-supported $

printer-stacking-order-supported $

printer-output-features-supported )

)

3.3.  printerService

This structural class defines printer information.  It is derived

from class printerAbstract and thus inherits common printer

attributes.  This class can be used with or without auxiliary classes

to define printer information.  Auxiliary classes can be used to

extend the common printer information with protocol, service or

operating system specific information.  Note that when extending

other structural classes with auxiliary classes, printerService MUST

NOT be used.

LDAP applications SHOULD use printer-uri as the naming attribute.

That is, when using printerService, printer-uri SHOULD be used as the

attribute type of the directory entry's relative distinguished name

(RDN).  printer-uri uniquely identifies each of the printer services

for a given printer.  Note that if the printer service changes

domains, printer-uri MUST be updated with the new domain name.

( 1.3.18.0.2.6.255

NAME  'printerService'

DESC  'Printer information.'

STRUCTURAL

SUP   printerAbstract

MAY   ( printer-uri $ printer-xri-supported )

)

3.4.  printerServiceAuxClass

This auxiliary class defines printer information.  It is derived from

class printerAbstract and thus inherits common printer attributes.

This class MUST be used with a structural class.

LDAP applications SHOULD use printer-uri as the naming attribute.

That is, when using printerServiceAuxClass, printer-uri SHOULD be

used as the attribute type of the directory entry's relative

distinguished name (RDN).  printer-uri uniquely identifies each of

the printer services for a given printer.  Note that if the printer

service changes domains, printer-uri MUST be updated with the new

domain name.

( 1.3.18.0.2.6.257

NAME  'printerServiceAuxClass'

DESC  'Printer information.'

Fleming, Jones, Lewis, McDonald    Expires 28 February 2002     [Page 7]

Internet Draft      LDAP Schema for Printer Services      28 August 2001

AUXILIARY

SUP   printerAbstract

MAY   ( printer-uri $ printer-xri-supported )

)

3.5.  printerIPP

This auxiliary class defines Internet Printing Protocol (IPP/1.1)

[RFC2911] information.  It MUST be used with a structural class such

as printerService.  It is used to extend structural classes with IPP

specific printer information.

( 1.3.18.0.2.6.256

NAME  'printerIPP'

DESC  'Internet Printing Protocol (IPP) information.'

AUXILIARY

SUP   top

MAY   ( printer-ipp-versions-supported $

printer-multiple-document-jobs-supported )

)

3.6.  printerLPR

This auxiliary class defines LPR [RFC1179] information.  It MUST be

used with a structural class such as printerService.  It is used to

identify directory entries that support LPR.

( 1.3.18.0.2.6.253

NAME  'printerLPR'

DESC  'LPR information.'

AUXILIARY

SUP   top

MUST ( printer-name )

MAY ( printer-aliases)

)

Fleming, Jones, Lewis, McDonald    Expires 28 February 2002     [Page 8]

Internet Draft      LDAP Schema for Printer Services      28 August 2001

4.  Definition of Attribute Types

The following attribute types are referenced by the object classes

defined in Section 3.

The following attribute types reference syntax OIDs defined in

Section 6 of [RFC2252] (see Section 5 'Definition of Syntaxes'

below).

The following attribute types reference matching rule names (instead

of OIDs) for clarity (see Section 6 below).  Note that if the printer

information is not known, the attribute value is not set (for

optional attributes).  In the following definitions, referenced

matching rules are defined in Section 8 of [RFC2252] and/or Section 6

of [X.520].  (see Section 6 'Definition of Matching Rules' below).

Note:  Some implementations of LDAP servers do not support some or

all of the [X.520] matching rules in the EQUALITY, ORDERING, or

SUBSTR clauses of attribute definitions.  Administrators may wish to:

1) Omit the EQUALITY clause (or at least the 'booleanMatch', which is

not defined in [RFC2252]);

2) Omit the ORDERING clause (or at least the 'integerOrderingMatch',

which is not defined in [RFC2252]);

3) Omit the SUBSTR clause.

The following table is a summary of the attribute names defined by

this document and their corresponding names from [RFC2911].  Some

attribute names described in [RFC2911] have been prefixed with

'printer-' as recommended in [RFC2926], to address the flat namespace

for LDAP identifiers.

LDAP & SLP Printer Schema       IPP Model [RFC2911]

------------------------------  -------------------------------------

printer-uri

printer-xri-supported

[IPP printer-uri-supported]

[IPP uri-authentication-supported]

[IPP uri-security-supported]

printer-name                    printer-name

printer-natural-language-configured

natural-language-configured

printer-location                printer-location

printer-info                    printer-info

printer-more-info               printer-more-info

printer-make-and-model          printer-make-and-model

printer-ipp-versions-supported  ipp-versions-supported

Fleming, Jones, Lewis, McDonald    Expires 28 February 2002     [Page 9]

Internet Draft      LDAP Schema for Printer Services      28 August 2001

printer-multiple-document-jobs-supported

multiple-document-jobs-supported

printer-charset-configured      charset-configured

printer-charset-supported       charset-supported

printer-generated-natural-language-supported

generated-natural-language-supported

printer-document-format-supported

document-format-supported

printer-color-supported         color-supported

printer-compression-supported   compression-supported

printer-pages-per-minute        pages-per-minute

printer-pages-per-minute-color  pages-per-minute-color

printer-finishings-supported    finishings-supported

printer-number-up-supported     number-up-supported

printer-sides-supported         sides-supported

printer-media-supported         media-supported

printer-media-local-supported   [site names from IPP media-supported]

printer-resolution-supported    printer-resolution-supported

printer-print-quality-supported print-quality-supported

printer-job-priority-supported  job-priority-supported

printer-copies-supported        copies-supported

printer-job-k-octets-supported  job-k-octets-supported

printer-current-operator

printer-service-person

printer-delivery-orientation-supported

printer-stacking-order-supported

printer-output-features-supported

printer-aliases

4.1.  printer-uri

Note, that for SLP registered printers, the LDAP printer-uri

attribute MUST set to the value of the registered URL of the printer.

( 1.3.18.0.2.4.1140

NAME 'printer-uri'

DESC 'A URI supported by this printer.

This URI SHOULD be used as a relative distinguished name (RDN).

If printer-xri-supported is implemented, then this URI value

MUST be listed in a member value of printer-xri-supported.'

EQUALITY caseIgnoreMatch

ORDERING caseIgnoreOrderingMatch

SUBSTR caseIgnoreSubstringsMatch

SYNTAX  1.3.6.1.4.1.1466.115.121.1.15

SINGLE-VALUE

)

Fleming, Jones, Lewis, McDonald    Expires 28 February 2002    [Page 10]

Internet Draft      LDAP Schema for Printer Services      28 August 2001

4.2.  printer-xri-supported

A list of XRI (extended resource identifiers) supported by this

printer.  Each value of this list consists of a URI (uniform resource

identifier) followed by optional authentication and security

metaparameters.  The keywords for URI and their metaparameters are:

'uri'  == IPP 'printer-uri-supported' value

'auth' == IPP 'uri-authentication-supported' value

'sec'  == IPP 'uri-security-supported' value

Legal values of the 'auth' metaparameter include

'none' (no authentication for this URI)

'requesting-user-name' (from operation request)

'basic' (HTTP/1.1 Basic [RFC2617])

'digest' (HTTP/1.1 Basic, [RFC2617])

'certificate' (from certificate)

per IPP Model [3] (extensions MAY also be used).  A missing 'auth'

metaparameter SHALL mean 'none'.  Legal values of the 'sec'

metaparameter include

'none' (no security for this URI)

'ssl3' (Netscape SSL3)

'tls' (IETF TLS/1.0, [RFC2246])

per IPP Model [3] (extensions MAY also be used).  A missing 'sec'

metaparameter SHALL mean 'none'.  Each metaparameter of a list member

is delimited by '<'.  For example:

'uri=ipp://foo.com< auth=digest< sec=tls<'

'uri=lpr://bar.com< auth=none< sec=none<'

Registrations MAY consolidate values for metaparameters, as in the

following example:

'uri=ipp://foo.com< auth=basic,digest< sec=tls,ssl3<'

( 1.3.18.0.2.4.1107

NAME 'printer-xri-supported'

DESC 'The unordered list of XRI (extended resource identifiers)

supported by this printer.  Each member of the list consists of

a URI (uniform resource identifier) followed by optional

authentication and security metaparameters.'

EQUALITY caseIgnoreMatch

ORDERING caseIgnoreOrderingMatch

SUBSTR caseIgnoreSubstringsMatch

SYNTAX 1.3.6.1.4.1.1466.115.121.1.15

)

4.3.  printer-name

The site-specific administrative name of this printer.  This value of

this attribute SHOULD be in the language specified in

'printer-natural-language-configured' (although the printer's name

MAY be in any language).  This name MAY be the last part of the

Fleming, Jones, Lewis, McDonald    Expires 28 February 2002    [Page 11]

Internet Draft      LDAP Schema for Printer Services      28 August 2001

printer's URI or it MAY be completely unrelated.  This name MAY

contain characters that are not allowed in a conventional URI (which

conforms to [RFC2396]).

( 1.3.18.0.2.4.1135

NAME 'printer-name'

DESC 'The site-specific administrative name of this printer, more

end-user friendly than a URI.'

EQUALITY caseIgnoreMatch

ORDERING caseIgnoreOrderingMatch

SUBSTR caseIgnoreSubstringsMatch

SYNTAX  1.3.6.1.4.1.1466.115.121.1.15{127}

SINGLE-VALUE

)

4.4.  printer-natural-language-configured

( 1.3.18.0.2.4.1119

NAME 'printer-natural-language-configured'

DESC 'The configured language in which error and status messages will

be generated (by default) by this printer.  Also, a possible

language for printer string attributes set by operator, system

administrator, or manufacturer.  Also, the (declared) language

of the "printer-name", "printer-location", "printer-info", and

"printer-make-and-model" attributes of this printer. For

example: "en-us" (US English) or "fr-fr" (French in France)

Legal values of language tags conform to [RFC3066] "Tags for

the Identification of Languages".'

EQUALITY caseIgnoreMatch

ORDERING caseIgnoreOrderingMatch

SUBSTR caseIgnoreSubstringsMatch

SYNTAX  1.3.6.1.4.1.1466.115.121.1.15{127}

SINGLE-VALUE

)

4.5.  printer-location

( 1.3.18.0.2.4.1136

NAME 'printer-location'

DESC 'Identifies the location of the printer. This could include

things like: "in Room 123A", "second floor of building XYZ".'

EQUALITY caseIgnoreMatch

ORDERING caseIgnoreOrderingMatch

SUBSTR caseIgnoreSubstringsMatch

SYNTAX  1.3.6.1.4.1.1466.115.121.1.15{127}

SINGLE-VALUE

)

Fleming, Jones, Lewis, McDonald    Expires 28 February 2002    [Page 12]

Internet Draft      LDAP Schema for Printer Services      28 August 2001

4.6.  printer-info

( 1.3.18.0.2.4.1139

NAME 'printer-info'

DESC 'Identifies the descriptive information about this printer.

This could include things like: "This printer can be used for

printing color transparencies for HR presentations", or "Out

of courtesy for others, please print only small (1-5 page) jobs

at this printer", or even "This printer is going away on July

1, 1997, please find a new printer".'

EQUALITY caseIgnoreMatch

ORDERING caseIgnoreOrderingMatch

SUBSTR caseIgnoreSubstringsMatch

SYNTAX  1.3.6.1.4.1.1466.115.121.1.15{127}

SINGLE-VALUE

)

4.7.  printer-more-info

( 1.3.18.0.2.4.1134

NAME 'printer-more-info'

DESC 'A URI used to obtain more information about this specific

printer.  For example, this could be an HTTP type URI

referencing an HTML page accessible to a Web Browser.  The

information obtained from this URI is intended for end user

consumption.'

EQUALITY caseIgnoreMatch

ORDERING caseIgnoreOrderingMatch

SUBSTR caseIgnoreSubstringsMatch

SYNTAX  1.3.6.1.4.1.1466.115.121.1.15

SINGLE-VALUE

)

4.8.  printer-make-and-model

( 1.3.18.0.2.4.1138

NAME 'printer-make-and-model'

DESC 'Identifies the make and model of the device.  The device

manufacturer MAY initially populate this attribute.'

EQUALITY caseIgnoreMatch

ORDERING caseIgnoreOrderingMatch

SUBSTR caseIgnoreSubstringsMatch

SYNTAX  1.3.6.1.4.1.1466.115.121.1.15{127}

SINGLE-VALUE

)

Fleming, Jones, Lewis, McDonald    Expires 28 February 2002    [Page 13]

Internet Draft      LDAP Schema for Printer Services      28 August 2001

4.9.  printer-ipp-versions-supported

( 1.3.18.0.2.4.1133

NAME 'printer-ipp-versions-supported'

DESC 'Identifies the IPP protocol version(s) that this printer

supports, including major and minor versions, i.e., the version

numbers for which this Printer implementation meets the

conformance requirements.'

EQUALITY caseIgnoreMatch

ORDERING caseIgnoreOrderingMatch

SUBSTR caseIgnoreSubstringsMatch

SYNTAX  1.3.6.1.4.1.1466.115.121.1.15{127}

)

4.10.  printer-multiple-document-jobs-supported

( 1.3.18.0.2.4.1132

NAME 'printer-multiple-document-jobs-supported'

DESC 'Indicates whether or not the printer supports more than one

document per job, i.e., more than one Send-Document or

Send-Data operation with document data.'

EQUALITY booleanMatch

SYNTAX  1.3.6.1.4.1.1466.115.121.1.7

SINGLE-VALUE

)

4.11.  printer-charset-configured

( 1.3.18.0.2.4.1109

NAME 'printer-charset-configured'

DESC 'The configured charset in which error and status messages will

be generated (by default) by this printer.  Also, a possible

charset for printer string attributes set by operator, system

administrator, or manufacturer.  For example: "utf-8" (ISO

10646/Unicode) or "iso-8859-1" (Latin1).  Legal values are

defined by the IANA Registry of Coded Character Sets and the

"(preferred MIME name)" SHALL be used as the tag.  For

coherence with IPP Model, charset tags in this attribute SHALL

be lowercase normalized.  This attribute SHOULD be static (time

of registration) and SHOULD NOT be dynamically refreshed

(subsequently).'

EQUALITY caseIgnoreMatch

SYNTAX  1.3.6.1.4.1.1466.115.121.1.15{63}

SINGLE-VALUE

)

Fleming, Jones, Lewis, McDonald    Expires 28 February 2002    [Page 14]

Internet Draft      LDAP Schema for Printer Services      28 August 2001

4.12.  printer-charset-supported

( 1.3.18.0.2.4.1131

NAME 'printer-charset-supported'

DESC 'Identifies the set of charsets supported for attribute type

values of type Directory String for this directory entry.  For

example: "utf-8" (ISO 10646/Unicode) or "iso-8859-1" (Latin1).

Legal values are defined by the IANA Registry of Coded

Character Sets and the preferred MIME name.'

EQUALITY caseIgnoreMatch

SYNTAX  1.3.6.1.4.1.1466.115.121.1.15{63}

)

4.13.  printer-generated-natural-language-supported

( 1.3.18.0.2.4.1137

NAME 'printer-generated-natural-language-supported'

DESC 'Identifies the natural language(s) supported for this directory

entry.  For example: "en-us" (US English) or "fr-fr" (French in

France).  Legal values conform to [RFC3066], Tags for the

Identification of Languages.'

EQUALITY caseIgnoreMatch

ORDERING caseIgnoreOrderingMatch

SUBSTR caseIgnoreSubstringsMatch

SYNTAX  1.3.6.1.4.1.1466.115.121.1.15{63}

)

4.14.  printer-document-format-supported

( 1.3.18.0.2.4.1130

NAME 'printer-document-format-supported'

DESC 'The possible document formats in which data may be interpreted

and printed by this printer.  Legal values are MIME types come

from the IANA Registry of Internet Media Types.'

EQUALITY caseIgnoreMatch

SYNTAX  1.3.6.1.4.1.1466.115.121.1.15{127}

)

4.15.  printer-color-supported

( 1.3.18.0.2.4.1129

NAME 'printer-color-supported'

DESC 'Indicates whether this printer is capable of any type of color

printing at all, including highlight color.'

EQUALITY booleanMatch

SYNTAX  1.3.6.1.4.1.1466.115.121.1.7

Fleming, Jones, Lewis, McDonald    Expires 28 February 2002    [Page 15]

Internet Draft      LDAP Schema for Printer Services      28 August 2001

SINGLE-VALUE

)

4.16.  printer-compression-supported

( 1.3.18.0.2.4.1128

NAME 'printer-compression-supported'

DESC 'Compression algorithms supported by this printer.  For example:

"deflate, gzip".  Legal values include; "none", "deflate"

(public domain ZIP), "gzip" (GNU ZIP), "compress" (UNIX).'

EQUALITY caseIgnoreMatch

SYNTAX  1.3.6.1.4.1.1466.115.121.1.15{255}

)

4.17.  printer-pages-per-minute

( 1.3.18.0.2.4.1127

NAME 'printer-pages-per-minute'

DESC 'The nominal number of pages per minute which may be output by

this printer (e.g., a simplex or black-and-white printer).

This attribute is informative, NOT a service guarantee.

Typically, it is the value used in marketing literature to

describe this printer.'

EQUALITY integerMatch

ORDERING integerOrderingMatch

SYNTAX  1.3.6.1.4.1.1466.115.121.1.27

SINGLE-VALUE

)

4.18.  printer-pages-per-minute-color

( 1.3.18.0.2.4.1126

NAME 'printer-pages-per-minute-color'

DESC 'The nominal number of color pages per minute which may be

output by this printer (e.g., a simplex or color printer).

This attribute is informative, NOT a service guarantee.

Typically, it is the value used in marketing literature to

describe this printer.'

EQUALITY integerMatch

ORDERING integerOrderingMatch

SYNTAX  1.3.6.1.4.1.1466.115.121.1.27

SINGLE-VALUE

)

Fleming, Jones, Lewis, McDonald    Expires 28 February 2002    [Page 16]

Internet Draft      LDAP Schema for Printer Services      28 August 2001

4.19.  printer-finishings-supported

( 1.3.18.0.2.4.1125

NAME 'printer-finishings-supported'

DESC 'The possible finishing operations supported by this printer.

Legal values include; "none", "staple", "punch", "cover",

"bind", "saddle-stitch", "edge-stitch", "staple-top-left",

"staple-bottom-left", "staple-top-right",

"staple-bottom-right", "edge-stitch-left", "edge-stitch-top",

"edge-stitch-right", "edge-stitch-bottom", "staple-dual-left",

"staple-dual-top", "staple-dual-right", "staple-dual-bottom".'

EQUALITY caseIgnoreMatch

SUBSTR caseIgnoreSubstringsMatch

SYNTAX  1.3.6.1.4.1.1466.115.121.1.15{255}

)

4.20.  printer-number-up-supported

( 1.3.18.0.2.4.1124

NAME 'printer-number-up-supported'

DESC 'The possible numbers of print-stream pages to impose upon a

single side of an instance of a selected medium. Legal values

include; 1, 2, and 4.  Implementations may support other

values.'

EQUALITY integerMatch

ORDERING integerOrderingMatch

SYNTAX  1.3.6.1.4.1.1466.115.121.1.27

)

4.21.  printer-sides-supported

( 1.3.18.0.2.4.1123

NAME 'printer-sides-supported'

DESC 'The number of impression sides (one or two) and the two-sided

impression rotations supported by this printer.  Legal values

include; "one-sided", "two-sided-long-edge",

"two-sided-short-edge".'

EQUALITY caseIgnoreMatch

SYNTAX  1.3.6.1.4.1.1466.115.121.1.15{127}

)

4.22.  printer-media-supported

( 1.3.18.0.2.4.1122

NAME 'printer-media-supported'

DESC 'The standard names/types/sizes (and optional color suffixes) of

Fleming, Jones, Lewis, McDonald    Expires 28 February 2002    [Page 17]

Internet Draft      LDAP Schema for Printer Services      28 August 2001

the media supported by this printer.  For example: "iso-a4",

"envelope", or "na-letter-white".  Legal values  conform to ISO

10175, Document Printing Application (DPA), and any IANA

registered extensions.'

EQUALITY caseIgnoreMatch

SYNTAX  1.3.6.1.4.1.1466.115.121.1.15{255}

)

4.23.  printer-media-local-supported

( 1.3.18.0.2.4.1117

NAME 'printer-media-local-supported'

DESC 'Site-specific names of media supported by this printer, in the

language in "printer-natural-language-configured".

For example: "purchasing-form" (site-specific name) as opposed

to (in "printer-media-supported"): "na-letter" (standard

keyword from ISO 10175).'

EQUALITY caseIgnoreMatch

SUBSTR caseIgnoreSubstringsMatch

SYNTAX  1.3.6.1.4.1.1466.115.121.1.15{255}

)

4.24.  printer-resolution-supported

( 1.3.18.0.2.4.1121

NAME 'printer-resolution-supported'

DESC 'List of resolutions supported for printing documents by this

printer.  Each resolution value is a string with 3 fields:

1) Cross feed direction resolution (positive integer), 2) Feed

direction resolution (positive integer), 3) Resolution unit.

Legal values are "dpi" (dots per inch) and "dpcm" (dots per

centimeter).  Each resolution field is delimited by ">".  For

example:  "300> 300> dpi>".'

EQUALITY caseIgnoreMatch

SUBSTR caseIgnoreSubstringsMatch

SYNTAX  1.3.6.1.4.1.1466.115.121.1.15{255}

)

4.25.  printer-print-quality-supported

( 1.3.18.0.2.4.1120

NAME 'printer-print-quality-supported'

DESC 'List of print qualities supported for printing documents on

this printer.  For example: "draft, normal".  Legal values

include; "unknown", "draft", "normal", "high".'

EQUALITY caseIgnoreMatch

SYNTAX  1.3.6.1.4.1.1466.115.121.1.15{127}

)

Fleming, Jones, Lewis, McDonald    Expires 28 February 2002    [Page 18]

Internet Draft      LDAP Schema for Printer Services      28 August 2001

4.26.  printer-job-priority-supported

( 1.3.18.0.2.4.1110

NAME 'printer-job-priority-supported'

DESC 'Indicates the number of job priority levels supported.  An IPP

conformant printer which supports job priority must always

support a full range of priorities from "1" to "100" (to ensure

consistent behavior), therefore this attribute describes the

"granularity".  Legal values of this attribute are from "1" to

"100".'

EQUALITY integerMatch

ORDERING integerOrderingMatch

SYNTAX  1.3.6.1.4.1.1466.115.121.1.27

SINGLE-VALUE

)

4.27.  printer-copies-supported

( 1.3.18.0.2.4.1118

NAME 'printer-copies-supported'

DESC 'The maximum number of copies of a document that may be printed

as a single job.  A value of "0" indicates no maximum limit.  A

value of "-1" indicates unknown.'

EQUALITY integerMatch

ORDERING integerOrderingMatch

SYNTAX  1.3.6.1.4.1.1466.115.121.1.27

SINGLE-VALUE

)

4.28.  printer-job-k-octets-supported

( 1.3.18.0.2.4.1111

NAME 'printer-job-k-octets-supported'

DESC 'The maximum size in kilobytes (1,024 octets actually) incoming

print job that this printer will accept.  A value of "0"

indicates no maximum limit.  A value of "-1" indicates

unknown.'

EQUALITY integerMatch

ORDERING integerOrderingMatch

SYNTAX  1.3.6.1.4.1.1466.115.121.1.27

SINGLE-VALUE

)

Fleming, Jones, Lewis, McDonald    Expires 28 February 2002    [Page 19]

Internet Draft      LDAP Schema for Printer Services      28 August 2001

4.29.  printer-current-operator

( 1.3.18.0.2.4.1112

NAME 'printer-current-operator'

DESC 'The name of the current human operator responsible for

operating this printer.  It is suggested that this string

include information that would enable other humans to reach the

operator, such as a phone number.'

EQUALITY caseIgnoreMatch

ORDERING caseIgnoreOrderingMatch

SUBSTR caseIgnoreSubstringsMatch

SYNTAX  1.3.6.1.4.1.1466.115.121.1.15{127}

SINGLE-VALUE

)

4.30.  printer-service-person

( 1.3.18.0.2.4.1113

NAME 'printer-service-person'

DESC 'The name of the current human service person responsible for

servicing this printer.  It is suggested that this string

include information that would enable other humans to reach the

service person, such as a phone number.'

EQUALITY caseIgnoreMatch

ORDERING caseIgnoreOrderingMatch

SUBSTR caseIgnoreSubstringsMatch

SYNTAX  1.3.6.1.4.1.1466.115.121.1.15{127}

SINGLE-VALUE

)

4.31.  printer-delivery-orientation-supported

( 1.3.18.0.2.4.1114

NAME 'printer-delivery-orientation-supported'

DESC 'The possible delivery orientations of pages as they are printed

and ejected from this printer.  Legal values include;

"unknown", "face-up", and "face-down".'

EQUALITY caseIgnoreMatch

SYNTAX  1.3.6.1.4.1.1466.115.121.1.15{127}

)

4.32.  printer-stacking-order-supported

( 1.3.18.0.2.4.1115

NAME 'printer-stacking-order-supported'

DESC 'The possible stacking order of pages as they are printed and

Fleming, Jones, Lewis, McDonald    Expires 28 February 2002    [Page 20]

Internet Draft      LDAP Schema for Printer Services      28 August 2001

ejected from this printer. Legal values include; "unknown",

"first-to-last", "last-to-first".'

EQUALITY caseIgnoreMatch

SYNTAX  1.3.6.1.4.1.1466.115.121.1.15{127}

)

4.33.  printer-output-features-supported

( 1.3.18.0.2.4.1116

NAME 'printer-output-features-supported'

DESC 'The possible output features supported by this printer. Legal

values include; "unknown", "bursting", "decollating",

"page-collating", "offset-stacking".'

EQUALITY caseIgnoreMatch

SYNTAX  1.3.6.1.4.1.1466.115.121.1.15{127}

)

4.34.  printer-aliases

( 1.3.18.0.2.4.1108

NAME 'printer-aliases'

DESC 'Site-specific administrative names of this printer in addition

the printer name specified for printer-name.'

EQUALITY caseIgnoreMatch

ORDERING caseIgnoreOrderingMatch

SUBSTR caseIgnoreSubstringsMatch

SYNTAX  1.3.6.1.4.1.1466.115.121.1.15{127}

)

Fleming, Jones, Lewis, McDonald    Expires 28 February 2002    [Page 21]

Internet Draft      LDAP Schema for Printer Services      28 August 2001

5.  Definition of Syntaxes

No new attribute syntaxes are defined by this document.

The attribute types defined in Section 4 above reference syntax OIDs

defined in Section 6 of [RFC2252], which are summarized below:

Syntax OID                      Syntax Description

------------------------------  ------------------

1.3.6.1.4.1.1466.115.121.1.7    Boolean

1.3.6.1.4.1.1466.115.121.1.15   Directory String (UTF-8 [RFC2279])

1.3.6.1.4.1.1466.115.121.1.27   Integer

6.  Definition of Matching Rules

No new matching rules are defined by this document.

The attribute types defined in Section 4 above reference matching

rules defined in Section 8 of [RFC2252] and/or Section 6 of [X.520],

which are summarized below:

Matching Rule OID               Matching Rule Name          Usage

------------------------------  ------------------          -----

2.5.13.13*                      booleanMatch                EQUALITY

2.5.13.2                        caseIgnoreMatch             EQUALITY

2.5.13.14                       integerMatch                EQUALITY

2.5.13.3                        caseIgnoreOrderingMatch     ORDERING

2.5.13.15*                      integerOrderingMatch        ORDERING

2.5.13.4                        caseIgnoreSubstringsMatch   SUBSTR

* - Defined in ITU-T X.520:1996 [X.520] but not listed in [RFC2252]

Note:  Some implementations of LDAP servers do not support some or

all of the [X.520] matching rules in the EQUALITY, ORDERING, or

SUBSTR clauses of attribute definitions.  Administrators may wish to:

1) Omit the EQUALITY clause (or at least the 'booleanMatch', which is

not defined in [RFC2252]);

2) Omit the ORDERING clause (or at least the 'integerOrderingMatch',

which is not defined in [RFC2252]);

3) Omit the SUBSTR clause.

Fleming, Jones, Lewis, McDonald    Expires 28 February 2002    [Page 22]

Internet Draft      LDAP Schema for Printer Services      28 August 2001

7.  IANA Considerations

There are no IANA registration considerations defined by this

document.

8.  Internationalization Considerations

All text string attribute values in objects of the printerService

class MUST be encoded in UTF-8 [RFC2279] characters, as required by

the syntax 'Directory String' [RFC2252].  Also, a language tag

[RFC3066] for all of the text string attributes in objects of the

printerService class SHOULD be supplied in

'printer-natural-language-configured'.  Therefore, all objects of the

printerService class conform to the "IETF Policy on Character Sets

and Languages" [RFC2277].

9.  Security Considerations

As with any LDAP schema, it is important to protect specific entries

and attributes with the appropriate access control.  It is

particularly important that only administrators can modify entries

defined in this LDAP printer schema.  For additional considerations

of deploying printers in an IPP environment, the reader is referred

to Section 8 of [RFC2911].

Obtaining a reference to an object and storing it in the directory

may make a handle to the object available to a wider audience.  This

may have security implications.

10.  References

[SLPPRT] St. Pierre, Isaacson, McDonald.  Definition of the Printer

Abstract Service Type v2.0, <durable URL below>, May 2000.

Reviewed and approved by IETF SLP Designated Expert, according to

Section 5 'IANA Considerations' in [RFC2609].

Archived in the IANA SLP Template Registry:

ftp://isi.edu/in-notes/iana/assignments/svrloc-templates/

in the file 'printer.2.0.en'

[RFC1179] McLaughlin.  Line Printer Daemon Protocol, RFC 1179, August

1990.

[RFC2119] Bradner.  Key words for use in RFCs to Indicate Requirement

Levels, RFC 2119, March 1997.

Fleming, Jones, Lewis, McDonald    Expires 28 February 2002    [Page 23]

Internet Draft      LDAP Schema for Printer Services      28 August 2001

[RFC2246] Dierks, Allen.  TLS Protocol Version 1.0, RFC 2246, January

1999.

[RFC2251] Wahl, Howes, Kille.  Lightweight Directory Access Protocol

(v3), RFC 2251, December 1997.

[RFC2252] Wahl, Coulbeck, Howes, Kille.  Lightweight Directory Access

Protocol (v3): Attribute Syntax Definitions, RFC 2252, December 1997.

[RFC2277] Alvestrand.  IETF Policy on Character Sets and Languages,

RFC 2277, January 1998.

[RFC2279] Yergeau.  UTF-8, a Transformation Format of ISO 10646, RFC

2279, January 1998.

[RFC2396] Berners-Lee, Fielding, Masinter.  URI Generic Syntax, RFC

2396, August 1998.

[RFC2608] Guttman, Perkins, Veizades, Day.  Service Location Protocol

v2, RFC 2608, June 1999.

[RFC2609] Guttman, Perkins, Kempf.  Service Templates and Service:

Schemes, RFC 2609, June 1999.

[RFC2617] Franks, Hallam-Baker, Hostetler, Lawrence, Leach, Luotonen,

Stewart.  HTTP Authentication:  Basic and Digest Access

Authentication, RFC 2617, June 1999.

[RFC2911] deBry, Hastings, Herriot, Isaacson, Powell.  Internet

Printing Protocol/1.1: Model and Semantics, RFC 2911, September 2000.

[RFC2926] Kempf, Moats, St. Pierre.  Conversion of LDAP Schemas to

and from SLP Templates, RFC 2926, September 2000.

[RFC3066] Alvestrand.  Tags for the Identification of Languages, RFC

3066, January 2001.

[X.520] The Directory: Selected Attribute Types.  ITU-T

Recommendation X.520 and ISO/IEC 9594-6, 1993.

11.  Acknowledgments

Thanks to the members of the IPP Working group, Kimberly Reger (IBM),

Robert Moore (IBM) and Lee Rafalow (IBM), and Kurt Zeilenga

(OpenLDAP) for their review comments and help in preparing this

document.

Fleming, Jones, Lewis, McDonald    Expires 28 February 2002    [Page 24]

Internet Draft      LDAP Schema for Printer Services      28 August 2001

12.  Authors' Addresses

Principal Editor:

Pat Fleming

IBM

Highway 52 N.

Rochester, MN 55901

USA

Phone: +1 507-253-7583

EMail: flemingp@us.ibm.com

Ken Jones

eStarCom

400 S McCaslin Blvd Suite 211

Louisville, CO  80027

USA

Phone: +1 720-890-7507

EMail: kenjones@estarcom.com

Harry Lewis

IBM

6300 Diagonal Hwy

Boulder, CO  80301

USA

Phone: +1 303-924-5337

EMail: harryl@us.ibm.com

Ira McDonald

High North Inc

221 Ridge Ave

Grand Marais, MI 49839

USA

Phone: +1 906-494-2434

Email: imcdonald@crt.xerox.com

Fleming, Jones, Lewis, McDonald    Expires 28 February 2002    [Page 25]

Internet Draft      LDAP Schema for Printer Services      28 August 2001

13.  Full Copyright Statement

Copyright (C) The Internet Society (2001).  All Rights Reserved.

This document and translations of it may be copied and furnished to

others, and derivative works that comment on or otherwise explain it

or assist in its implementation may be prepared, copied, published

and distributed, in whole or in part, without restriction of any

kind, provided that the above copyright notice and this paragraph are

included on all such copies and derivative works.  However, this

document itself may not be modified in any way, such as by removing

the copyright notice or references to the Internet Society or other

Internet organizations, except as needed for the purpose of

developing Internet standards in which case the procedures for

copyrights defined in the Internet Standards process must be

followed, or as required to translate it into languages other than

English.

The limited permissions granted above are perpetual and will not be

revoked by the Internet Society or its successors or assigns.

This document and the information contained herein is provided on an

"AS IS" basis and THE INTERNET SOCIETY AND THE INTERNET ENGINEERING

TASK FORCE DISCLAIMS ALL WARRANTIES, EXPRESS OR IMPLIED, INCLUDING

BUT NOT LIMITED TO ANY WARRANTY THAT THE USE OF THE INFORMATION

HEREIN WILL NOT INFRINGE ANY RIGHTS OR ANY IMPLIED WARRANTIES OF

MERCHANTABILITY OR FITNESS FOR A PARTICULAR PURPOSE."

Fleming, Jones, Lewis, McDonald    Expires 28 February 2002    [Page 26]