Service Location Working Group                           Pete St. Pierre

INTERNET DRAFT                                          Sun Microsystems

Expires 31 July 2000                                      Scott Isaccson

Novell

Ira McDonald

High North

31 January 2000

Definition of the Printer Abstract Service Type

<draft-ietf-svrloc-printer-scheme-05.txt>

Status of This Memo

This document is an Internet-Draft and is in full conformance with

all provisions of Section 10 of RFC2026.  Internet-Drafts are working

documents of the Internet Engineering Task Force (IETF), its areas,

and its working groups.  Note that other groups may also distribute

working documents as Internet-Drafts.

Internet-Drafts are draft documents valid for a maximum of six months

and may be updated, replaced, or obsoleted by other documents at any

time.  It is inappropriate to use Internet-Drafts as reference

material or to cite them other than as "work in progress."

To view the list of Internet-Draft Shadow Directories, see

http://www.ietf.org/shadow.html.

Abstract

This document is a product of the Service Location and Internet

Printing Protocol Working Groups of the Internet Engineering Task

Force (IETF).  Comments should be sent to the srvloc@srvloc.org and

ipp@pwg.org mailing lists.

This document defines the 'printer:' abstract service type and the

attributes associated with it.  This 'printer:' service template is

designed to be used in conjunction with the Service Location

Protocol, Version 2 (SLPv2) [13], but may be used with any directory

service which supports attribute/value pair registration, such as the

Lightweight Directory Access Protocol, Version 3 (LDAPv3, RFC 2251).

The 'printer:' service type is specified as an abstract service type.

Printers advertised with the 'printer:' abstract service type may be

accessible by one or more print protocols, such as IPP [3] and LPR

[2].

St. Pierre, Isaacson, McDonald       Expires 31 July 2000       [Page 1]

Internet Draft       Printer Abstract Service Type       30 January 2000

Table of Contents

1.  Introduction ...............................................       3

2.  Terminology ................................................       3

3.  Template url-path Definition ...............................       4

3.1.  IPP ....................................................       4

3.2.  LPR ....................................................       4

4.  Printer Service Template ...................................       5

5.  Summary of Required Attributes .............................      15

5.1.  Rationale for Required Attributes ......................      15

6.  Summary of Optional Attributes .............................      16

6.1.  Rationale for Optional Attributes ......................      16

7.  Summary of Attribute Origins ...............................      18

8.  IANA Considerations ........................................      19

9.  Internationalization Considerations ........................      19

10.  Security Considerations ...................................      19

11.  References ................................................      20

12.  Acknowledgments ...........................................      21

13.  Authors' Addresses ........................................      21

14.  Full Copyright Statement ..................................      22

St. Pierre, Isaacson, McDonald       Expires 31 July 2000       [Page 2]

Internet Draft       Printer Abstract Service Type       30 January 2000

1.  Introduction

Service Type templates are used to describe in a standard way those

services which use the 'service:' URL.  The template described in

this document is an abstract service type that includes concrete

types such as the printing protocol defined in RFC 1179 [2], "Line

Printer Daemon Protocol".  The service type for this 'service:' URL

is 'printer:'.

The 'printer:' abstract service type supports consistent registration

of printer services.  The attributes described within this document

are derived from previous specifications developed by the IETF IPP WG

and IETF Printer MIB WG.

The attributes specified are intended to facilitate both automatic

and manual selection of services, not to provide service state,

statistics, or notification.  The target audience of service

attributes consists of users, either software agents or end users.

2.  Terminology

The key words "MUST", "MUST NOT", "REQUIRED", "SHALL", "SHALL NOT",

"SHOULD", "SHOULD NOT", "RECOMMENDED", "MAY", and "OPTIONAL" in this

document are to be interpreted as described in RFC 2119 [14].

St. Pierre, Isaacson, McDonald       Expires 31 July 2000       [Page 3]

Internet Draft       Printer Abstract Service Type       30 January 2000

3.  Template url-path Definition

The 'printer:' type is an abstract service type.  Because an abstract

service type may contain one of many concrete types, the 'url-path'

associated with a 'printer:' service URL may vary.  IPP and LPR

printers are presently supported by this 'printer:' template.  Other

printer protocols MAY be supported by extension templates or by

future updates of this abstract 'printer:' template.

3.1.  IPP

An IPP Printer object is defined in "IPP/1.1 Model and Semantics"

[3].  An IPP printer concrete URL is defined in "IPP/1.1 Encoding and

Transport" [9].

Examples of valid 'service:' URLs for IPP printers include:

service:printer:ipp://server.sun.com/cgi-bin/public-printer

service:printer:ipp://foo.sun.com/printers?public-printer

3.2.  LPR

An LPR accessible printer MAY include a queue name as the last part

of the URL.  If the queue name is absent, the print server is assumed

to use a default print queue.  The definition of an LPR printer

concrete URL is specified in this document, in the 'printer:' service

template.

Examples of valid 'service:' URLs for LPR printers include:

service:printer:lpr://server.sun.com

service:printer:lpr://server.sun.com/public-printer

St. Pierre, Isaacson, McDonald       Expires 31 July 2000       [Page 4]

Internet Draft       Printer Abstract Service Type       30 January 2000

4.  Printer Service Template

The 'printer:' service template defined below conforms to the grammar

described in "Service Templates and service: Schemes".  Please refer

to [4] for detailed explanation of the syntax.

Name of submitters: Pete St. Pierre <Pete.StPierre@eng.sun.com>

Scott Isaacson <sisaacson@novell.com>

Ira McDonald <imcdonald@sharplabs.com>

Language of service template: en (English)

Security Considerations:

By advertising the security methods associated with each supported

printer URL via the mandatory attributes 'printer-uri-supported'

'uri-authentication-supported', and 'uri-security-supported', the

the printer may expose information useful to attackers.  SLPv2

security or another security method SHOULD be used to authenticate

any service advertisements.

Template Text:

-------------------- template begins here --------------------

template-type = printer

template-version = 1.0

template-description =

The 'printer:' service template describes the attributes

supported by network printing devices.  Devices may be

either directly connected to a network or managed by a

print server.  The device or server understands one or

more network print protocols such as IPP or LPR.

template-url-syntax =

url-path    = ippurl / lprurl

ippurl      = IPP URL as defined in [9]

lprurl      = "lpr://" hostport [ "/" qname ]

hostport    = host [ ":" port ]

host        = hostname / hostnumber

hostname    = *( domainlabel "." ) toplabel

domainlabel = alphanum /

alphanum * [alphanum / "-"] alphanum

toplabel    = alpha / alpha * [alphanum / "-"] alphanum

hostnumber  = ipv4-number / ipv6-number

ipv4-number = 1*3digit 3*3("." 1*3digit)

ipv6-number = 32*hex

3digit      = digit digit digit

port        = 1*digit

alphanum    = alpha / digit

St. Pierre, Isaacson, McDonald       Expires 31 July 2000       [Page 5]

Internet Draft       Printer Abstract Service Type       30 January 2000

alpha       = "a" / "b" / "c" / "d" / "e" / "f" / "g" /

"h" / "i" / "j" / "k" / "l" / "m" / "n" /

"o" / "p" / "q" / "r" / "s" / "t" / "u" /

"v" / "w" / "x" / "y" / "z" /

"A" / "B" / "C" / "D" / "E" / "F" / "G" /

"H" / "I" / "J" / "K" / "L" / "M" / "N" /

"O" / "P" / "Q" / "R" / "S" / "T" / "U" /

"V" / "W" / "X" / "Y" / "Z"

digit       = "0" / "1" / "2" / "3" / "4" / "5" / "6" /

"7" / "8" / "9"

printer-uri-supported = STRING L

# REQUIRED for all registrations by conforming SLP SAs

# IPP 'printer-uri-supported'

# The ORDERED list of URI supported by this printer,

# correlated with 'uri-authentication-supported' values

# and correlated with 'uri-security-supported' values.

# Each list member (including the last) is delimited by '>'.

# For example:

#   'lpr://foo.com> ipp://bar.com>'

uri-authentication-supported = STRING L

# REQUIRED for all registrations by conforming SLP SAs

# IPP 'uri-authentication-supported'

# The ORDERED list of authentication supported for each URI

# specified in 'printer-uri-supported' for this printer.

# Each list member (including the last) is delimited by '>'.

# For example:

#   'none> basic> certificate>'

# (see example of 'printer-uri-supported' above).

# Legal values include

#   'none' (no authentication for this URI)

#   'requesting-user-name' (from operation request)

#   'basic' (HTTP/1.1 Basic, RFC 2617)

#   'digest' (HTTP/1.1 Basic, RFC 2617)

#   'certificate' (from certificate)

# per IPP Model [3] (extensions MAY also be used).

# URI that do not support authentication SHALL specify

# 'none'.

uri-security-supported = STRING L

# REQUIRED for all registrations by conforming SLP SAs

# IPP 'uri-security-supported'

# The ORDERED list of security supported for each URI

# specified in 'printer-uri-supported' for this printer.

# Each list member (including the last) is delimited by '>'.

# For example:

#   'none> tls>'

# (see example of 'printer-uri-supported' above).

# Legal values include

#   'none' (no security for this URI)

St. Pierre, Isaacson, McDonald       Expires 31 July 2000       [Page 6]

Internet Draft       Printer Abstract Service Type       30 January 2000

#   'ssl3' (Netscape SSL3)

#   'tls' (IETF TLS/1.0, RFC 2246)

# per IPP Model [3] (extensions MAY also be used).

# URI that do not support security SHALL specify

# 'none'.

printer-name = STRING

# REQUIRED for all registrations by conforming SLP SAs

# IPP 'printer-name'

# The site-specific administrative name of this printer,

# in the language in 'natural-language-configured'.

# This name MAY be the last part of the printer's URI or it

# MAY be completely unrelated.

# This name MAY contain characters that are not allowed in a

# conventional URI (which conforms to RFC 2396).

# If this printer information is not known to the SLP SA,

# then this attribute SHALL be set to 'unknown'.

# This attribute SHOULD be static (time of registration)

# and SHOULD NOT be dynamically refreshed (subsequently).

printer-location = STRING O

unknown

# IPP 'printer-location'

# The physical location of this printer,

# in the language in 'natural-language-configured'.

# A free form description of this printer's physical

# location, for example:

#   'Orlando office, 2nd floor, near the fire escape'

# If this printer information is not known to the SLP SA,

# then this attribute SHALL be set to 'unknown'.

# However, it is STRONGLY RECOMMENDED that this attribute

# be supported and that it be set to a meaningful value so

# that users can determine this printer's physical location

# for printer selection (before print job submission) and

# for output collection (after print job completion).

printer-info = STRING O

unknown

# IPP 'printer-info'

# Additional descriptive information on this printer,

# in the language in 'natural-language-configured'.

# A free form string that may contain any site-specific

# descriptive information about this printer.

# If this printer information is not known to the SLP SA,

# then this attribute SHALL be set to 'unknown'.

printer-more-info = STRING L O

unknown

# IPP 'printer-more-info'

# A URI used to obtain more information about this specific

# printer.  For example, this could be an 'http:' URI

St. Pierre, Isaacson, McDonald       Expires 31 July 2000       [Page 7]

Internet Draft       Printer Abstract Service Type       30 January 2000

# referencing an HTML page accessible to a Web Browser.

# The information obtained from this URI is intended for

# end user consumption.

# If this printer information is not known to the SLP SA,

# then this attribute SHALL be set to 'unknown'.

printer-make-and-model = STRING O

unknown

# IPP 'printer-make-and-model'

# The manufacturer, make, and model of this printer,

# a simple text string defined by the manufacturer,

# in the language in 'natural-language-configured'.

# If this printer information is not known to the SLP SA,

# then this attribute SHALL be set to 'unknown'.

ipp-versions-supported = STRING L M O

none

# IPP 'ipp-versions-supported'

# The unordered list of 'major.minor' IPP versions

# supported by this printer or 'none'.

# For example:

#   '1.0, 1.1'

# Legal values include 'none', '1.0', and '1.1',

# per IPP Model [3] (extensions MAY also be used).

# If this printer information is not known to the SLP SA,

# then this attribute SHALL be set to 'none'.

multiple-document-jobs-supported = STRING L O

unknown

# IPP 'multiple-document-jobs-supported'

# Indicates whether this printer supports more than one

# document per job.

# This template attribute is an extended boolean.

# If this printer information is not known to the SLP SA,

# then this attribute SHALL be set to 'unknown'.

unknown, true, false

charset-configured = STRING L O

utf-8

# IPP 'charset-configured'

# The configured charset in which error and status messages

# will be generated (by default) by this printer.

# Also, a possible charset for printer string attributes

# set by operator, system administrator, or manufacturer.

# For example:

#   'utf-8' (ISO 10646/Unicode) or 'iso-8859-1' (Latin1)

# Legal values of charset tags (names/aliases) come from

# the IANA Registry of Coded Character Sets [6] and

# the '(preferred MIME name)' SHALL be used as the tag.

# For coherence with IPP Model [3], charset tags in this

# attribute SHALL be lowercase normalized.

St. Pierre, Isaacson, McDonald       Expires 31 July 2000       [Page 8]

Internet Draft       Printer Abstract Service Type       30 January 2000

# This attribute SHOULD be static (time of registration)

# and SHOULD NOT be dynamically refreshed (subsequently).

charset-supported = STRING L M O

utf-8

# IPP 'charset-supported'

# The possible charsets in which error and status messages

# may be generated (if requested) by this printer.

# Also, the possible charsets for printer string attributes

# set by operator, system administrator, or manufacturer.

# For example:

#   'utf-8' (ISO 10646/Unicode) or 'iso-8859-1' (Latin1)

# Legal values of charset tags (names/aliases) come from

# the IANA Registry of Coded Character Sets [6] and

# the '(preferred MIME name)' SHALL be used as the tag.

# This attribute SHALL include the value 'utf-8', per

# RFC 2277, 'IETF Policy on Charsets and Languages' [12].

# For coherence with IPP Model [3], charset tags in this

# attribute SHALL be lowercase normalized.

natural-language-configured = STRING L

# REQUIRED for all registrations by conforming SLP SAs

# IPP 'natural-language-configured'

# The configured language in which error and status messages

# will be generated (by default) by this printer.

# Also, a possible language for printer string attributes

# set by operator, system administrator, or manufacturer.

# Also, the (declared) language of the 'printer-name',

# 'printer-location', 'printer-info', and

# 'printer-make-and-model' attributes of this printer.

# For example:

#   'en-us' (US English) or 'fr-fr' (French in France)

# Legal values of language tags conform to RFC 1766

# 'Tags for the Identification of Languages' [5].

# For coherence with IPP Model [3], language tags in this

# attribute SHALL be lowercase normalized.

# This attribute SHOULD be static (time of registration)

# and SHOULD NOT be dynamically refreshed (subsequently).

natural-language-supported = STRING L M

# REQUIRED for all registrations by conforming SLP SAs

# IPP 'generated-natural-language-supported'

# The possible languages in which error and status messages

# may be generated (if requested) by this printer.

# Also, the possible languages for printer string attributes

# set by operator, system administrator, or manufacturer.

# For example:

#   'en-us' (US English) or 'fr-fr' (French in France)

# Legal values of language tags conform to RFC 1766

# 'Tags for the Identification of Languages' [5].

# For coherence with IPP Model [3], language tags in this

St. Pierre, Isaacson, McDonald       Expires 31 July 2000       [Page 9]

Internet Draft       Printer Abstract Service Type       30 January 2000

# attribute SHALL be lowercase normalized.

document-format-supported = STRING L M

# REQUIRED for all registrations by conforming SLP SAs

# IPP 'document-format-supported'

# The possible document formats in which data may be

# interpreted and printed by this printer.

# Legal values of document formats (MIME types) come from

# the IANA Registry of Internet Media Types [11].

# If this printer information is not known to the SLP SA,

# then this attribute SHALL be set to 'unknown'.

color-supported = STRING L O

unknown

# IPP 'color-supported'

# Indicates whether this printer is capable of any type of

# color printing at all, including highlight color.

# This template attribute is an extended boolean.

# If this printer information is not known to the SLP SA,

# then this attribute SHALL be set to 'unknown'.

unknown, true, false

compression-supported = STRING L M

# REQUIRED for all registrations by conforming SLP SAs

# IPP 'compression-supported'

# The unordered list of compression algorithms supported

# by this printer.

# For example:

#   'deflate, gzip'

# Legal values include

#   'none'

#   'deflate' (public domain ZIP)

#   'gzip' (GNU ZIP)

#   'compress' (UNIX)

# per IPP Model [3] (extensions MAY also be used).

# If this printer information is not known to the SLP SA,

# then this attribute SHALL be set to 'none'.

pages-per-minute = INTEGER O

-1

# IPP 'pages-per-minute'

# The nominal number of pages per minute which may be

# output by this printer (e.g., simplex, black-and-white).

# This attribute is informative, NOT a service guarantee.

# Typically, it is the value used in marketing literature

# to describe this printer.

# A value of '-1' indicates unknown.

# If this printer information is not known to the SLP SA,

# then this attribute SHALL be set to '-1'.

pages-per-minute-color = INTEGER O

St. Pierre, Isaacson, McDonald      Expires 31 July 2000       [Page 10]

Internet Draft       Printer Abstract Service Type       30 January 2000

-1

# IPP 'pages-per-minute-color'

# The nominal number of color pages per minute which may be

# output by this printer (e.g., simplex, color).

# This attribute is informative, NOT a service guarantee.

# Typically, it is the value used in marketing literature

# to describe this printer.

# A value of '-1' indicates unknown.

# If this printer information is not known to the SLP SA,

# then this attribute SHALL be set to '-1'.

finishings-supported = STRING L M O

none

# IPP 'finishings-supported'

# The possible finishing operations supported by this

# printer.

# Legal values of finishings are defined in IPP Model [3].

# If this printer information is not known to the SLP SA,

# then this attribute SHALL be set to 'none'.

none, staple, punch, cover, bind,

saddle-stitch, edge-stitch,

staple-top-left, staple-bottom-left,

staple-top-right, staple-bottom-right,

edge-stitch-left, edge-stitch-top,

edge-stitch-right, edge-stitch-bottom,

staple-dual-left, staple-dual-top,

staple-dual-right, staple-dual-bottom

number-up-supported = INTEGER M O

1

# IPP 'number-up-supported'

# The possible numbers of print-stream pages to impose

# upon a single side of an instance of a selected

# medium.

# Legal values of this attribute include 1, 2, and 4 [3].

# Implementations may support other values.

# If this printer information is not known to the SLP SA,

# then this attribute SHALL be set to '1'.

sides-supported = STRING L M O

one-sided

# IPP 'sides-supported'

# (Compare with Salutation 'duplex-mode')

# The number of impression sides (one or two) and the

# two-sided impression rotations supported by this printer.

# Salutation 'simplex' == IPP 'one-sided'

# Salutation 'duplex' == IPP 'two-sided-long-edge'

# Salutation 'tumble' == IPP 'two-sided-short-edge'

# If this printer information is not known to the SLP SA,

# then this attribute SHALL be set to 'one-sided'.

one-sided, two-sided-long-edge, two-sided-short-edge

St. Pierre, Isaacson, McDonald      Expires 31 July 2000       [Page 11]

Internet Draft       Printer Abstract Service Type       30 January 2000

media-supported = STRING L M O

unknown

# IPP 'media-supported' - only the standard keyword values

# The standard names/types/sizes (and optional color

# suffixes) of the media supported by this printer.

# The values specified are NOT localized according to the

# value of 'natural-language-configured', but are in a

# fixed language of 'en-us' (US English).  For example:

#   'iso-a4' or 'envelope' or 'na-letter-white'

# Legal values of this attribute conform to ISO 10175

# 'Document Printing Application (DPA)' [10] and

# any IANA registered extensions, per IPP Model [3].

# If this printer information is not known to the SLP SA,

# then this attribute SHALL be set to 'unknown'.

media-local-supported = STRING M O

unknown

# IPP 'media-supported' - only site-specific name values

# Site-specific names of media supported by this printer,

# in the language in 'natural-language-configured'.

# For example:

#   'purchasing-form' (site-specific name)

# as opposed to (in 'media-supported' above):

#   'na-letter' (standard keyword from ISO 10175 [10]).

# If this printer information is not known to the SLP SA,

# then this attribute SHALL be set to 'unknown'.

printer-resolution-supported = STRING L M O

unknown

# IPP 'printer-resolution-supported'

# (Compare with 'printer-uri-supported' in this template)

# The unordered list of resolutions supported for printing

# documents by this printer.

# Each resolution supported is a string with 3 fields:

# 1) Crossfeed direction resolution (positive integer)

# 2) Feed direction resolution (positive integer)

# 3) Resolution unit (enumerated value - see below)

# Each resolution field is delimited by '>', for example:

#   '300> 300> dpi>, 600> 600> dpi>'

# Legal values of resolution unit are

#   'dpi' (dots per inch)

#   'dpcm' (dots per centimeter)

# per IPP Model [3] (extensions SHOULD NOT be used).

# This attribute is derived from the Printer MIB [7].

# If this printer information is not known to the SLP SA,

# then this attribute SHALL be set to 'unknown'.

print-quality-supported = STRING L M O

unknown

# IPP 'print-quality-supported'

St. Pierre, Isaacson, McDonald      Expires 31 July 2000       [Page 12]

Internet Draft       Printer Abstract Service Type       30 January 2000

# The unordered list of print qualities supported for

# printing documents on this printer.

# For example:

#   'draft, normal'

# Legal values are defined in IPP Model [3].

# If this printer information is not known to the SLP SA,

# then this attribute SHALL be set to 'unknown'.

unknown, draft, normal, high

job-priority-supported = INTEGER O

1

# IPP 'job-priority-supported'

# (Compare with Salutation 'priority-levels-supported')

# Indicates the number of job priority levels supported.

# An IPP conformant printer which supports job priority

# must always support a full range of priorities from

# '1' to '100' (to ensure consistent behavior), therefore

# this template attribute describes the 'granularity'.

# Legal values of this attribute are from '1' to '100'.

# If this printer information is not known to the SLP SA,

# then this attribute SHALL be set to '1'.

copies-supported = INTEGER O

-1

# IPP 'copies-supported'

# The maximum number of copies of a document

# that may be printed as a single job.

# A value of '0' indicates no maximum limit.

# A value of '-1' indicates unknown.

# If this printer information is not known to the SLP SA,

# then this attribute SHALL be set to '-1'.

job-k-octets-supported = INTEGER O

-1

# IPP 'job-k-octets-supported'

# The maximum size in kilobytes (1,024 octets actually)

# incoming print job that this printer will accept.

# A value of '0' indicates no maximum limit.

# A value of '-1' indicates unknown.

# If this printer information is not known to the SLP SA,

# then this attribute SHALL be set to '-1'.

printer-current-operator = STRING M O

unknown

# Printer MIB 'prtGeneralCurrentOperator'

# The name of the current human operator responsible for

# operating this printer.  It is suggested that this string

# include information that would enable other humans to

# reach the operator, such as a phone number.

# If this printer information is not known to the SLP SA,

# then this attribute SHALL be set to 'unknown'.

St. Pierre, Isaacson, McDonald      Expires 31 July 2000       [Page 13]

Internet Draft       Printer Abstract Service Type       30 January 2000

# This attribute SHOULD be static (time of registration)

# and SHOULD NOT be dynamically refreshed (subsequently).

printer-service-person = STRING M O

unknown

# Printer MIB 'prtGeneralServicePerson'

# The name of the current service person responsible for

# servicing this printer.  It is suggested that this string

# include information that would enable other humans to

# reach the service person, such as a phone number.

# If this printer information is not known to the SLP SA,

# then this attribute SHALL be set to 'unknown'.

# This attribute SHOULD be static (time of registration)

# and SHOULD NOT be dynamically refreshed (subsequently).

delivery-orientation-supported = STRING L O

unknown

# Printer MIB 'prtOutputPageDeliveryOrientation'

# The possible delivery orientations of pages as they are

# printed and ejected from this printer.

# If this printer information is not known to the SLP SA,

# then this attribute SHALL be set to 'unknown'.

unknown, face-up, face-down

stacking-order-supported = STRING L M O

unknown

# Printer MIB 'prtOutputStackingOrder'

# (Compare with Salutation 'paper-output')

# The possible stacking order of pages as they are printed

# and ejected from this printer.

# If this printer information is not known to the SLP SA,

# then this attribute SHALL be set to 'unknown'.

unknown, first-to-last, last-to-first

output-features-supported = STRING L M O

unknown

# Printer MIB 'prtOutputFeaturesGroup'

# (Compare with Salutation 'paper-output')

# The possible output features supported by this printer.

# 'bursting' == Printer MIB 'prtOutputBursting'

# 'decollating' == Printer MIB 'prtOutputDecollating'

# 'page-collating' == Printer MIB 'prtOutputPageCollated'

# 'offset-stacking' == Printer MIB 'prtOutputOffestStacking'

# If this printer information is not known to the SLP SA,

# then this attribute SHALL be set to 'unknown'.

unknown, bursting, decollating, page-collating,

offset-stacking

-------------------- template ends here ----------------------

St. Pierre, Isaacson, McDonald      Expires 31 July 2000       [Page 14]

Internet Draft       Printer Abstract Service Type       30 January 2000

5.  Summary of Required Attributes

Attributes are associated with 'service:' URLs in order to provide a

dynamic search capability to service location clients, not to burden

servers implementations during registrations.

A small subset (8) of the attributes defined in 'printer:' are

REQUIRED in all compliant service registrations by SLP SAs:

SLP Required Attribute                  IPP Generic Directory Schema

----------------------                  ----------------------------

printer-uri-supported                   r

uri-authentication-supported            r

uri-security-supported                  r

printer-name                            r

natural-language-configured             m (SLP enhancement)

natural-language-supported              o (SLP enhancement)

document-format-supported               r

compression-supported                   r

r   RECOMMENDED - Appendix E 'Generic Directory Schema' IPP Model [3]

REQUIRED - SLP 'printer:' template

o   OPTIONAL - Appendix E 'Generic Directory Schema' IPP Model [3]

REQUIRED - SLP 'printer:' template

m   Missing - Appendix E 'Generic Directory Schema' IPP Model [3]

REQUIRED - SLP 'printer:' template

5.1.  Rationale for Required Attributes

'natural-language-configured'

- REQUIRED in SLP 'printer:' template to specify language tags for

'printer-name', 'printer-location', 'printer-info', and

'printer-make-and-model' attributes;

- missing in Appendix E 'Generic Directory Schema' of IPP Model [3],

because the corresponding IPP attributes are language tagged in-band

via the IPP 'textWithLanguage' syntax.

'natural-language-supported'

- REQUIRED in SLP 'printer:' template to assist users in selecting

appropriate printers;

- missing in Appendix E 'Generic Directory Schema' of IPP Model [3].

All other REQUIRED SLP 'printer:' template attributes are RECOMMENDED

in Appendix E 'Generic Directory Schema' IPP Model [3].

St. Pierre, Isaacson, McDonald      Expires 31 July 2000       [Page 15]

Internet Draft       Printer Abstract Service Type       30 January 2000

6.  Summary of Optional Attributes

Many of the attributes defined in 'printer:' are OPTIONAL in all

compliant service registrations by SLP SAs:

SLP Optional Attribute                  IPP Generic Directory Schema

----------------------                  ----------------------------

printer-location                        r

printer-info                            o

printer-more-info                       o

printer-make-and-model                  r

ipp-versions-supported                  r

multiple-document-jobs-supported        o

charset-configured                      m (SLP enhancement)

charset-supported                       o

color-supported                         r

finishings-supported                    r

number-up-supported                     o

sides-supported                         r

media-supported                         r

media-local-supported                   m (part of 'media-supported')

pages-per-minute                        o

pages-per-minute-color                  o

printer-resolution-supported            o

print-quality-supported                 o

job-priority-supported                  m (SLP enhancement)

copies-supported                        m (SLP enhancement)

job-k-octets-supported                  m (SLP enhancement)

printer-current-operator                m (from Printer MIB)

printer-service-person                  m (from Printer MIB)

delivery-orientation-supported          m (from Printer MIB)

stacking-order-supported                m (from Printer MIB)

output-features-supported               m (from Printer MIB)

r   RECOMMENDED - Appendix E 'Generic Directory Schema' IPP Model [3]

OPTIONAL - SLP 'printer:' template (with specified default)

o   OPTIONAL - Appendix E 'Generic Directory Schema' IPP Model [3]

OPTIONAL - SLP 'printer:' template (with specified default)

m   Missing - Appendix E 'Generic Directory Schema' IPP Model [3]

OPTIONAL - SLP 'printer:' template (with specified default)

6.1.  Rationale for Optional Attributes

'printer-location', 'printer-make-and-model', 'color-supported',

'finishings-supported', 'sides-supported', 'media-supported', and

'local-media-supported'

St. Pierre, Isaacson, McDonald      Expires 31 July 2000       [Page 16]

Internet Draft       Printer Abstract Service Type       30 January 2000

- OPTIONAL in SLP 'printer:' template because network print servers

may not be able to determine this information;

- RECOMMENDED in Appendix E 'Generic Directory Schema' of IPP Model

[3].

'ipp-versions-supported'

- OPTIONAL in SLP 'printer:' template because network printers may

not support IPP;

- RECOMMENDED in Appendix E 'Generic Directory Schema' of IPP Model

[3].

'charset-configured'

- OPTIONAL in SLP 'printer:' template to assist users in selecting

appropriate printers;

- missing in Appendix E 'Generic Directory Schema' of IPP Model [3].

'job-priority-supported', 'copies-supported', and

'job-k-octets-supported'

- OPTIONAL in SLP 'printer:' template to assist users in selecting

appropriate printers;

- missing in Appendix E 'Generic Directory Schema' of IPP Model [3].

'printer-current-operator', 'printer-service-person',

'delivery-orientation-supported', 'stacking-order-supported', and

'output-features-supported'

- OPTIONAL in SLP 'printer:' template to assist users in selecting

appropriate printers;

- missing in Appendix E 'Generic Directory Schema' of IPP Model [3],

because they are only specified in the Printer MIB [7], not in IPP.

All other OPTIONAL SLP 'printer:' template attributes are OPTIONAL in

Appendix E 'Generic Directory Schema' IPP Model [3].

St. Pierre, Isaacson, McDonald      Expires 31 July 2000       [Page 17]

Internet Draft       Printer Abstract Service Type       30 January 2000

7.  Summary of Attribute Origins

The following table summarizes the origins of all of the attributes

in the 'printer:' service template (except 'template-xxx' generic

attributes defined in "Service Templates and service: Schemes" [4]

and required for all 'service:' templates).

Attribute Name                          IPP[3]      Printer MIB[7]

--------------                          ------      --------------

printer-uri-supported                   X

uri-authentication-supported            X

uri-security-supported                  X

printer-name                            X

printer-location                        X

printer-info                            X

printer-more-info                       X

printer-make-and-model                  X

ipp-versions-supported                  X

multiple-document-jobs-supported        X

charset-configured                      X

charset-supported                       X

natural-language-configured             X

natural-language-supported              X

document-format-supported               X

color-supported                         X

compression-supported                   X

pages-per-minute                        X

pages-per-minute-color                  X

finishings-supported                    X

number-up-supported                     X

sides-supported                         X

media-supported                         X

media-local-supported                   X

printer-resolution-supported            X

print-quality-supported                 X

job-priority-supported                  X

copies-supported                        X

job-k-octets-supported                  X

printer-current-operator                            X

printer-service-person                              X

delivery-orientation-supported                      X

stacking-order-supported                            X

output-features-supported                           X

St. Pierre, Isaacson, McDonald      Expires 31 July 2000       [Page 18]

Internet Draft       Printer Abstract Service Type       30 January 2000

8.  IANA Considerations

Registration of this 'printer:' service template will follow the

procedures defined in section 4 'A Procedure for Standardizing New

Service Types' and section 5 'IANA Considerations' of "Service

Templates and service: Schemes" [4].

9.  Internationalization Considerations

All attribute values in registrations using this 'printer:' service

template MUST be encoded in UTF-8 characters, as required by "Service

Location Protocol, Version 2" [13].  Thus, all registrations using

this 'printer:' service template conform to "IETF Policy on Character

Sets and Languages" [12].

10.  Security Considerations

When used with SLPv2, this 'printer:' service template inherits all

of the security issues described in section 17 'Security

Considerations' of "Service Location Protocol, Version 2" [13].

St. Pierre, Isaacson, McDonald      Expires 31 July 2000       [Page 19]

Internet Draft       Printer Abstract Service Type       30 January 2000

11.  References

[1] J. Veizades, E. Guttman, C. Perkins, S. Kaplan.  Service Location

Protocol, RFC 2165, June 1997.

[2] L. McLaughlin.  Line Printer Daemon Protocol, RFC 1179, August

1990.

[3] R. deBry, T. Hastings, R. Herriot, S. Isaacson, P. Powell.

IPP/1.1:  Model and Semantics, <draft-ietf-ipp-model-v11-04.txt>

(work in progress), June 1999.

[4] E. Guttman, C. Perkins, J. Kempf.  Service Templates and service:

Schemes, RFC 2609, June 1999.  (Updates RFC 2165)

[5] H. Alvestrand.  Tags for the Identification of Languages, RFC

1766.  March 1995.

[6] IANA Registry of Coded Character Sets:

ftp://ftp.isi.edu/in-notes/iana/assignments/character-sets.

[7] R. Smith, F. Wright, T. Hastings, S. Zilles, J. Gyllenskog.

Printer MIB, RFC 1759, March 1995.

[8] Salutation Consortium, Inc.  Salutation Architecture

Specification V2.0, December 1996.

[9] R. Herriot, S. Butler, P. Moore, R. Turner.  IPP/1.1:  Encoding

and Transport, <draft-ietf-ipp-protocol-v11-03.txt> (work in

progress), June 1999.

[10] Information Technology - Document Printing Application (DPA),

ISO/IEC 10175, June 1996.

[11] IANA Registry of Internet Media Types (also called MIME types):

ftp://ftp.isi.edu/in-notes/iana/assignments/media-types

[12] H. Alvestrand.  IETF Policy on Character Sets and Languages, RFC

2277, January 1998.

[13] E. Guttman, C. Perkins, J. Veizades, M. Day.  Service Location

Protocol, Version 2, RFC 2608, June 1999.  (Updates RFC 2165)

[14] S. Bradner.  Key words for use in RFCs to Indicate Requirement

Levels, RFC 2119, March 1997.

St. Pierre, Isaacson, McDonald      Expires 31 July 2000       [Page 20]

Internet Draft       Printer Abstract Service Type       30 January 2000

12.  Acknowledgments

This document is a submission to the Service Location Working group.

Thanks to Jean Beha (Xerox), Jim Erwin (Novell), Tom Hastings

(Xerox), Bob Herriot (Xerox), James Kempf (Sun), Hugo Parra (Novell),

Todd Rupper (Novell), and Randy Turner (formerly Sharp).  Appendix E

'Generic Directory Schema' in IPP/1.1 Model [3] (recommended and

optional attributes for registering IPP printers) was the primary

input to this version of the 'printer:' service template.

13.  Authors' Addresses

Questions about this memo can be directed to:

Pete St. Pierre

Sun Microsystems

901 San Antonio Avenue

Palo Alto, CA 94043

USA

Phone: 650-786-5790

EMail: Pete.StPierre@eng.sun.com

Scott Isaccson

Novell

122 E 1700 S

Provo, UT 84606

USA

Phone: 801-861-7366

EMail: sisaacson@novell.com

Ira McDonald

High North

221 Ridge Ave

Grand Marais, MI 49839

USA

Phone: 906-494-2434 (or 2697)

Email: imcdonald@sharplabs.com

St. Pierre, Isaacson, McDonald      Expires 31 July 2000       [Page 21]

Internet Draft       Printer Abstract Service Type       30 January 2000

14.  Full Copyright Statement

Copyright (C) The Internet Society (1999).  All Rights Reserved.

This document and translations of it may be copied and furnished to

others, and derivative works that comment on or otherwise explain it

or assist in its implementation may be prepared, copied, published

and distributed, in whole or in part, without restriction of any

kind, provided that the above copyright notice and this paragraph are

included on all such copies and derivative works.  However, this

document itself may not be modified in any way, such as by removing

the copyright notice or references to the Internet Society or other

Internet organizations, except as needed for the purpose of

developing Internet standards in which case the procedures for

copyrights defined in the Internet Standards process must be

followed, or as required to translate it into languages other than

English.

The limited permissions granted above are perpetual and will not be

revoked by the Internet Society or its successors or assigns.

This document and the information contained herein is provided on an

"AS IS" basis and THE INTERNET SOCIETY AND THE INTERNET ENGINEERING

TASK FORCE DISCLAIMS ALL WARRANTIES, EXPRESS OR IMPLIED, INCLUDING

BUT NOT LIMITED TO ANY WARRANTY THAT THE USE OF THE INFORMATION

HEREIN WILL NOT INFRINGE ANY RIGHTS OR ANY IMPLIED WARRANTIES OF

MERCHANTABILITY OR FITNESS FOR A PARTICULAR PURPOSE."

St. Pierre, Isaacson, McDonald      Expires 31 July 2000       [Page 22]