-- The Input Switching Group

--

-- The input switching group allows the administrator to set the manual

-- input subunit timeout for the printer and to control the automatic

-- input subunit switching by the printer when an input subunit becomes

-- empty.

--

-- This group is optional. However, to claim conformance to this group,

-- it is required to implement every object in the group.

prtInputMediaLoadManualFeedTimeout OBJECT-TYPE

SYNTAX		Integer32

MAX-ACCESS	read-write

MIN-ACCESS	read-only

STATUS		current

DESCRIPTION

"The duration (in seconds) after which the printer shall

either:

(a) switch to another input subunit, if the value of

prtInputNextIndex is non-zero and prtInputAutoSwitch

is on(3)

or

(b) abort any job waiting for manually fed input, if the

value of prtInputNextIndex is zero or

prtInputAutoSwitch is off(4) or notPresent(5).

The event which causes the printer to enter the waiting state

is product specific. A value of (-1) implies 'other' or

'infinite' which translates to 'wait forever'.this input subunit doesn't

support manual feed'. A value of (-2) implies 'unknown'."

::= { prtInputEntry 24 }

prtInputAutoSwitch OBJECT-TYPE

SYNTAX		PresentOnOff

MAX-ACCESS	read-write

MIN-ACCESS	read-only

STATUS		current

DESCRIPTION

"Indicates the state of the auto input switching feature. The

value notPresent(5) indicates the feature is not currently

supported. Exact behavior of this feature is product specific."

::= { prtInputEntry 25 }

prtInputNextIndex OBJECT-TYPE

SYNTAX		Integer32

MAX-ACCESS	read-write

MIN-ACCESS	read-only

STATUS		current

DESCRIPTION

"The value of prtInputIndex corresponding to the input subunit

which will be used when this input subunit is emptied and the

timeout specified by prtInputMediaLoadTimeout expires. A value

of zero(0) indicates that auto input switching will not occur

when this input subunit is emptied."

::= { prtInputEntry 26 }