Finisher-MIB DEFINITIONS ::= BEGIN

IMPORTS

MODULE-IDENTITY, OBJECT-TYPE, experimental,

Integer32                                     FROM SNMPv2-SMI

TEXTUAL-CONVENTION                             FROM SNMPv2-TC

MODULE-COMPLIANCE, OBJECT-GROUP              FROM SNMPv2-CONF

hrDeviceIndex                         FROM HOST-RESOURCES-MIB

PrtSubUnitStatusTC,

PrtMarkerSuppliesSupplyUnitTC,

PrtCapacityUnitTC, prtOutputIndex,

PrtMarkerSuppliesClassTC, PresentOnOff,

PrtMediaPathIndex                            FROM Printer-MIB

finisherMIB MODULE-IDENTITY

LAST-UPDATED "9801120000Z"

ORGANIZATION "IETF Printer MIB Working Group"

CONTACT-INFO

"Ron Bergman

Dataproducts Corp.

1757 Tapo Canyon Road

Simi Valley, CA 91063-3394

rbergma@dpc.com

Send comments to the printmib WG using the Finisher MIB

Project (FIN) Mailing List:  fin@pwg.org

For further information, access the PWG web page under

'FIN':   http://www.pwg.org/"

DESCRIPTION

"The MIB module for management of printer finisher units.

The Finisher MIB is an extension of the Printer MIB."

::= { mib-2 43 }

ISSUE: Should this be in the PWG subtree or keep this as an extension to the Printer MIB?

-- Textual conventions for this MIB module

FinDeviceTypeTC ::= TEXTUAL-CONVENTION

-- This is a type 2 enumeration.

STATUS       current

DESCRIPTION

"The defined finishing device subunit operation

enumerations."

SYNTAX       INTEGER {

other(1),

unknown(2),

stitchingUnit(3),

foldingUnit(4),

bindingUnit(5),

trimmer(6),

dieCuttingUnit(7),

punchingUnit(8),

perforatingUnit(9),

slittingUnit(10),

separationCutUnit(11),

imprinter(12),

wrappingUnit(13),

bandingUnit(14)

}

FinSupplyTypeTC ::= TEXTUAL-CONVENTION

-- This is a type 2 enumeration that is an extension to the

-- Printer MIB textual convention PrtMarkerSuppliesTypeTC.

STATUS       current

DESCRIPTION

"The defined finishing supply type enumerations."

SYNTAX       INTEGER {

other(1),

unknown(2),

-- toner(3),

-- wasteToner(4),

-- ink(5),

-- inkCartridge(6),

-- inkRibbon(7),

-- wasteInk(8),

-- opc(9),                      -- photo conductor

-- developer(10),

-- fuserOil(11),

-- solidWax(12),

-- ribbonWax(13),

-- wasteWax(14),

-- fuser(15),

-- coronaWire(16),

-- fuserOilWick(17),

-- cleanerUnit(18),

-- fuserCleaningPad(19),

-- transferUnit(20),

-- tonerCartridge(21),

-- fuserOiler(22),

water(23),

wasteWater(24),

glueWaterAdditive(25),

wastePaper(26),

bindingTape(27),

bandingTape(28),

stitchingWire(29),

shrinkWrap(30),

paperWrap(31),

staples(32),

inserts(33),

covers(34)

}

FinStitchingTypeTC ::= TEXTUAL-CONVENTION

-- This is a type 2 enumeration.

STATUS       current

DESCRIPTION

"The defined stitching type enumerations."

SYNTAX       INTEGER {

other(1),

unknown(2),

staple(3),

stapleTopLeft(4),

stapleBottomLeft(5),

stapleTopRight(6),

stapleBottomRight(7),

saddleStitch(8),

edgeStitch(9),

stitch(10)

}

FinBindingTypeTC ::= TEXTUAL-CONVENTION

-- This is a type 2 enumeration.

STATUS       current

DESCRIPTION

"The defined binding type enumerations."

SYNTAX       INTEGER {

other(1),

unknown(2),

bind(3),

tape(4),

plastic(5),

velo(6),

perfect(7),

spiral(8)

}

FinSlittingTypeTC ::= TEXTUAL-CONVENTION

-- This is a type 2 enumeration.

STATUS       current

DESCRIPTION

"The defined slitting type enumerations."

SYNTAX       INTEGER {

other(1),

unknown(2),

slit(3),

slitAndSeparate(4),

slitAndMerge(5)

}

-- Finisher Device Group (Mandatory)

--

-- A printer may support zero or more finishing subunits.  A

-- finishing device subunit may be associated with one or more

-- output subunits and one or more media path subunits.

finDeviceTable OBJECT-TYPE

SYNTAX     SEQUENCE OF FinDeviceEntry

MAX-ACCESS not-accessible

STATUS     current

DESCRIPTION

"This table defines the finishing device subunits,

including information regarding possible configuration

options and the status for each finisher device subunit."

::= { finisherMIB 18 }

finDeviceEntry OBJECT-TYPE

SYNTAX      FinDeviceEntry

MAX-ACCESS  not-accessible

STATUS      current

DESCRIPTION

"There is an entry in the finishing device table for each

possible finisher operation."

INDEX  { hrDeviceIndex, finDeviceIndex }

::= { finDevicesTable 1 }

FinDeviceEntry ::= SEQUENCE {

finDeviceIndex                 Integer32,

finDeviceOperation             FinDeviceTypeTC,

finDevicePresentOnOff          PresentOnOff,

finDeviceCapacityUnit          PrtCapacityUnitTC,

finDeviceMaxCapacity           Integer32,

finDeviceRemainingCapacity     Integer32,

finDeviceAssociatedMediaPaths  Integer32,

finDeviceAssociatedOutputs     Integer32,

finDeviceStatus                PrtSubUnitStatusTC,

finDeviceName                  OCTET STRING,

finDeviceVendorName            OCTET STRING,

finDeviceModel                 OCTET STRING,

finDeviceVersion               OCTET STRING,

finDeviceSerialNumber          OCTET STRING,

finDeviceDescription           OCTET STRING

}

finDeviceIndex OBJECT-TYPE

SYNTAX      Integer32(0..2147483647)

MAX-ACCESS  not-accessible

STATUS      current

DESCRIPTION

"A unique value used to identify a finisher operation.

Although these values may change due to a major

reconfiguration of the printer system (e.g. the addition

of new finishing operations), the values are normally

expected to remain stable across successive power cycles."

::= { finDeviceEntry 1 }

finDeviceOperation OBJECT-TYPE

SYNTAX      FinDeviceTypeTC

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

"Defines the finishing operation associated with this table

row entry."

::= { finDeviceEntry 2 }

*****************************************************************

ISSUE: The finDeviceOperation object could be eliminated if finDeviceIndex was FinDeviceTypeTC.  This would depend upon the desirability of having table entries for all possible finisher functions.  The method defined here allows finDeviceIndex to be independent of the actual device.

*****************************************************************

finDevicePresentOnOff OBJECT-TYPE

SYNTAX      PresentOnOff

MAX-ACCESS  read-write

STATUS      current

DESCRIPTION

"Indicates if this finishing device subunit is available

and whether the device subunit is enabled."

::= { finDeviceEntry 3 }

*****************************************************************

ISSUE: This object provides no added value if a table entry is not included for devices that are not present.  This object should be changed to enabled/disabled status only.

*****************************************************************

finDeviceCapacityUnit OBJECT-TYPE

SYNTAX      PrtCapacityUnitTC

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

"The unit of measure for specifying the capacity of this

finisher device subunit."

::= { finDeviceEntry 4 }

finDeviceMaxCapacity OBJECT-TYPE

SYNTAX      Integer32

MAX-ACCESS  read-write

STATUS      current

DESCRIPTION

"The maximum capacity of this finisher device subunit in

finDeviceCapacityUnits.  If the device can reliably sense

this value, the value is sensed by the finisher device

and is read-only: otherwise the value may be written by a

management or control console application.  The value (-1)

means other and specifically indicates that the device

places no restrictions on this parameter.  The value (-2)

means unknown."

::= { finDeviceEntry 5 }

finDeviceCurrentCapacity OBJECT-TYPE

SYNTAX      Integer32

MAX-ACCESS  read-write

STATUS      current

DESCRIPTION

"The current capacity of this finisher device subunit in

finDeviceCapacityUnits.  If the device can reliably sense

this value, the value is sensed by the finisher and is

read-only: otherwise the value may be written by a

management or control console application.  The value (-1)

means other and specifically indicates that the device

places no restrictions on this parameter.  The value (-2)

means unknown."

::= { finDeviceEntry 6 }

finDeviceAssociatedMediaPaths OBJECT-TYPE

SYNTAX      Integer32

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

"Indicates the media paths which can supply media for this

finisher device.  The value of this object is a bit map

with each position representing the value of a

prtMediaPathIndex.  For a media path that can be a source

for this finisher device subunit, the bit position equal

to 2 raised to the power of one less than the value of

prtMediaPathIndex will be set.

For example, a value of 21 indicates the media paths with

a prtMediaPathIndex of 1 or 6 will supply media to this

finisher device subunit.

The most significant bit position SHALL not be used, which

allows a maximum of 31 media paths to be defined."

::= { finDeviceEntry 7 }

finDeviceAssociatedOutputs OBJECT-TYPE

SYNTAX      Integer32

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

"Indicates the printer output subunits this finisher device

subunit services.  The value of this object is a bit map

with each position representing the value of a

prtOutputIndex.  For an output subunit that is serviced

by this finisher device subunit, the bit position equal to

2 raised to the power of one less than the value of

prtOutputIndex will be set.

For example, a value of 49 indicates the output subunits

with a prtOutputIndex of 1, 4 or 7 can be serviced by this

finisher device subunit.

The most significant bit position SHALL not be used, which

allows a maximum of 31 output subunits to be defined."

::= { finDeviceEntry 8 }

finDeviceStatus OBJECT-TYPE

SYNTAX      PrtSubUnitStatusTC

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

"Indicates the current status of this finisher device

subunit."

::= { finDeviceEntry 9 }

-- The Extended Finisher Device Group

--

-- This group is optional.  However, to claim conformance to

-- this group, it is necessary to implement every object in the

-- group.

finDeviceName OBJECT-TYPE

SYNTAX      OCTET STRING(0..63)

MAX-ACCESS  read-write

STATUS      current

DESCRIPTION

"The name assigned to this finisher device subunit."

::= { finDeviceEntry 10 }

finDeviceVendorName OBJECT-TYPE

SYNTAX      OCTET STRING(0..63)

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

"The vendor name of this finisher device subunit."

::= { finDeviceEntry 11 }

finDeviceModel OBJECT-TYPE

SYNTAX      OCTET STRING(0..63)

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

"The model name of this finisher device subunit."

::= { finDeviceEntry 12 }

finDeviceVersion OBJECT-TYPE

SYNTAX      OCTET STRING(0..63)

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

"The version string for this finisher device subunit."

::= { finDeviceEntry 13 }

finDeviceSerialNumber OBJECT-TYPE

SYNTAX      OCTET STRING(0..63)

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

"The serial number assigned to this finisher device

subunit."

::= { finDeviceEntry 14 }

finDeviceDescription OBJECT-TYPE

SYNTAX      OCTET STRING(0..255)

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

"A free form text description of this device subunit in the

localization specified by prtGeneralCurrentLocalization."

::= { finDeviceEntry 15 }

*****************************************************************

ISSUE: The description object was discussed as a standard device subunit (not optional) in the LA meeting.  Its placement in the optional portion of the group is consistent with the Printer MIB input and output subgroups.

*****************************************************************

-- Finisher Supply Group

--

-- A finisher may have one or more supplies associated with it.

-- For example a finisher may use both binding tape and stitching

-- wire supplies. A finisher may also have more than one source

-- for a given type of supply e.g. multiple supply sources of ink

-- for imprinters.

finSupplyTable OBJECT-TYPE

SYNTAX     SEQUENCE OF FinSupplyEntry

MAX-ACCESS not-accessible

STATUS     current

DESCRIPTION

"Each unique source of supply is an entry in the finisher

supply table. Each supply entry has its own

characteristics associated with it such as colorant and

current supply level."

::= { finisherMIB 19 }

finSupplyEntry OBJECT-TYPE

SYNTAX     FinSupplyEntry

MAX-ACCESS not-accessible

STATUS     current

DESCRIPTION

"A list of finisher devices, with their associated

supplies and supplies characteristics."

INDEX  { hrDeviceIndex, finDeviceIndex, finSupplyIndex }

::= { finSupplyTable 1 }

FinSupplyEntry ::= SEQUENCE {

finSupplyIndex               Integer32,

finSupplyClass               PrtMarkerSuppliesClassTC,

finSupplyType                FinSupplyTypeTC,

finSupplyDescription         OCTET STRING,

finSupplyUnit                PrtMarkerSuppliesSupplyUnitTC,

finSupplyMaxCapacity         Integer32,

finSupplyCurrentLevel        Integer32,

finSupplyColorantValue       OCTET STRING

}

finSupplyIndex OBJECT-TYPE

SYNTAX      Integer32(0..2147483647)

MAX-ACCESS  not-accessible

STATUS      current

DESCRIPTION

"A unique value used by a finisher to identify this supply

container/receptacle.  Although these values may change

due to a major reconfiguration of the finisher (e.g. the

addition of new supply sources to the finisher), values

are normally expected to remain stable across successive

power cycles."

::= { finSupplyEntry 1 }

finSupplyClass OBJECT-TYPE

SYNTAX      PrtMarkerSuppliesClassTC

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

"This value indicates whether this supply entity

represents a supply that is consumed or a container that

is filled."

::= { finSupplyEntry 2 }

finSupplyType OBJECT-TYPE

SYNTAX      FinSupplyTypeTC

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

"The type of this supply."

::= { finSupplyEntry 3 }

finSupplyDescription OBJECT-TYPE

SYNTAX      OCTET STRING(0..255)

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

"The description of this supply/receptacle in text useful

for operators and management applications."

::= { finSupplyEntry 4 }

finSupplyUnit OBJECT-TYPE

SYNTAX      PrtMarkerSuppliesSupplyUnitTC

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

"Unit of measure of this finisher supply container or

receptacle."

::= { finSupplyEntry 5 }

finSupplyMaxCapacity OBJECT-TYPE

SYNTAX      Integer32

MAX-ACCESS  read-write

STATUS      current

DESCRIPTION

"The maximum capacity of this supply container/receptacle

expressed in Supply Units.  If this supply container/

receptacle can reliably sense this value, the value is

sensed  and is read-only; otherwise the value may be

written by a control panel or management application.  The

value (-1) means other and places no restrictions on this

parameter.  The value (-2) means unknown."

::= { finSupplyEntry 6 }

finSupplyCurrentLevel OBJECT-TYPE

SYNTAX      Integer32

MAX-ACCESS  read-write

STATUS      current

DESCRIPTION

"The current level if this supply is a container; the

remaining space if this supply is a receptacle. If this

supply container/receptacle can reliably sense this value,

the value is sensed  and is read-only; otherwise the value

may be written by a control panel or management

application.  The value (-1) means other and places no

restrictions on this parameter. The value (-2) means

unknown."

::= { finSupplyEntry 7 }

--             Capacity Attribute Relationships

--

--                 MEDIA INPUT MEASUREMENT

--

--     _______ |                   |

--      |      |                   |

--      |      |                   |                   |

--      |      |_ _ _ _ _ _ _ _ _ _| ________________  |direction  --      |      |                   |      |            v

-- MaxCapacity |                   |      |

--      |      | Sheets remaining  | CurrentLevel

--      |      |                   |      |

--      v      |                   |      v

--     ------- +-------------------+ -------

finSupplyColorantValue OBJECT-TYPE

SYNTAX      OCTET STRING(0..63)

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

"The name of the color of this colorant using standardized

string names from ISO 10175 (DPA) and ISO 10180 (SPDL)

which are: other, unknown, white, red, green, blue, cyan,

magenta, yellow and black.  Implementors may add

additional string values.  The naming conventions in ISO

9070 are recommended in order to avoid potential name

clashes."

::= { finSupplyEntry 8 }

-- Finisher Supply Media Input Group

--

-- A finisher device may have one or more associated supply media

-- inputs.  Each entry in this table defines an input for a

-- supply media type such as inserts, covers, etc.

finSupplyMediaInputTable OBJECT-TYPE

SYNTAX     SEQUENCE OF FinSupplyMediaInputEntry

MAX-ACCESS not-accessible

STATUS     current

DESCRIPTION

"The input subunits associated with a finisher supply media

are each represented by an entry in this table."

::= { finisherMIB 20 }

finSupplyMediaInputEntry OBJECT-TYPE

SYNTAX     FinSupplyMediaInputEntry

MAX-ACCESS not-accessible

STATUS     current

DESCRIPTION

"A list of finisher supply media input subunit features and

characteristics."

INDEX  { hrDeviceIndex, finDeviceIndex, finSupplyIndex,

finSupplyMediaInputIndex }

::= { finSupplyMediaInputTable 1 }

FinSupplyMediaInputEntry ::= SEQUENCE {

finSupplyMediaInputIndex            Integer32,

finSupplyMediaInputType             Integer32,

finSupplyMediaInputFeedControlMode  Integer32,

finSupplyMediaInputDimUnit          PrtCapacityUnitTC,

finSupplyMediaInputMediaDimFeedDir  Integer32,

finSupplyMediaInputMediaDimXFeedDir Integer32,

finSupplyMediaInputStatus           PrtSubUnitStatusTC,

finSupplyMediaInputMediaName        OCTET STRING,

finSupplyMediaInputName             OCTET STRING,

finSupplyMediaInputVendorName       OCTET STRING,

finSupplyMediaInputModel            OCTET STRING,

finSupplyMediaInputVersion          OCTET STRING,

finSupplyMediaInputSerialNumber     OCTET STRING,

finSupplyMediaInputDescription      OCTET STRING,

finSupplyMediaInputSecurity         PresentOnOff,

finSupplyMediaInputMediaWeight      Integer32,

finSupplyMediaInputMediaThickness   Integer32,

finSupplyMediaInputMediaType        OCTET STRING,

finSupplyMediaInputMediaColor       OCTET STRING,

finSupplyMediaInputMediaFormParts   Integer32

finSupplyMediaInputIndex OBJECT-TYPE

SYNTAX      Integer32(0..2147483647)

MAX-ACCESS  not-accessible

STATUS      current

DESCRIPTION

"A unique value used by a finisher to identify this supply

media input subunit.  Although these values may change

due to a major reconfiguration of the finisher (e.g. the

addition of new supply media input sources to the

finisher), values are normally expected to remain stable

across successive power cycles."

::= { finSupplyMediaInputEntry 1 }

finSupplyMediaInputType OBJECT-TYPE

SYNTAX      Integer32 {

other(1),

unknown(2),

removableBin(3),

nonRemovableBin(4),

manualFeed(5),

continuousRollDevice(6),

continuousFanFold(7)

****************************************************************

PrtInputTypeTC is similar except it does not have manualFeed and does have mailbox(6).  Can PrtInputTypeTC be used ?

****************************************************************

}

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

"The type of technology (discriminated primarily according

to the feeder mechanism type) employed by the input

subunit."

::= { finSupplyMediaInputEntry 2 }

finSupplyMediaInputFeedControlMode OBJECT-TYPE

SYNTAX      Integer32 {

other(1),

unknown(2),

feedOnly(3),

readAndFeed(4)

}

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

"This object defines the feeding mode for this finisher

supply media input.  feedOnly indicates the normal

feeding mode for this finisher input and no additional

information is needed to control the feeding process.

readAndFeed indicates that the feeding process is

controlled by scanning information on the input media.

When readAndFeed mode is selected, reader devices

associated with this input entry define the criteria that

must be met to trigger the feeder operation."

*****************************************************************

Is this object applicable ?

*****************************************************************

::= { finSupplyMediaInputEntry 3 }

finSupplyMediaInputDimUnit OBJECT-TYPE

SYNTAX      PrtCapacityUnitTC

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

"The unit of measure for specifying dimensional values for

this input device."

::= { finSupplyMediaInputEntry 4 }

finSupplyMediaInputMediaDimFeedDir OBJECT-TYPE

SYNTAX      Integer32

MAX-ACCESS  read-write

STATUS      current

DESCRIPTION

"This object provides the value of the dimension in the

feed direction of the media that is placed or will be

placed in this input device.  Feed dimension measurements

are taken parallel to the feed direction of the device and

measured in finSupplyMediaInputDimUnits.  If this input

device can reliably sense this value, the value is sensed

and is read-only access. Otherwise the value is read-write

access and may be written by management or control panel

applications. The value (-1) means other and specifically

indicates that this device places no restrictions on this

parameter. The value (-2) indicates unknown. "

::= { finSupplyMediaInputEntry 5 }

finSupplyMediaInputMediaDimXFeedDir OBJECT-TYPE

SYNTAX      Integer32

MAX-ACCESS  read-write

STATUS      current

DESCRIPTION

"This object provides the value of the dimension across the

feed direction of the media that is placed or will be

placed in this input device.  The cross feed direction is

ninety degrees relative to the feed direction on this

device and measured in finSupplyMediaInputDimUnits.  If

this input device can reliably sense this value, the value

is sensed and is read-only access. Otherwise the value is

read-write access and may be written by management or

control panel applications. The value (-1) means other and

specifically indicates that this device places no

restrictions on this parameter. The value (-2) indicates

unknown. "

::= { finSupplyMediaInputEntry 6 }

finSupplyMediaInputStatus OBJECT-TYPE

SYNTAX      PrtSubUnitStatusTC

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

"This value indicates the current status of this input

device."

::= { finSupplyMediaInputEntry 7 }

finSupplyMediaInputMediaName OBJECT-TYPE

SYNTAX      OCTET STRING(0..63)

MAX-ACCESS  read-write

STATUS      current

DESCRIPTION

"The name of the current media contained in this input

device. Examples are Print Job Output A, Triple A Billing

Statements or ISO standard names."

::= { finSupplyMediaInputEntry 8 }

-- Finisher Supply Media, Extended Input Group

--

-- This group is optional. However, to claim conformance to this

-- group it is necessary to implement every object in the group.

--

-- This group defines objects that augment the

-- finSupplyMediaInputType object for this input subunit.

finSupplyMediaInputName OBJECT-TYPE

SYNTAX      DisplayString(0..63)

MAX-ACCESS  read-write

STATUS      current

DESCRIPTION

"The name assigned to this input subunit."

::= { finSupplyMediaInputEntry 9 }

finSupplyMediaInputVendorName OBJECT-TYPE

SYNTAX      DisplayString(0..63)

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

"The vendor name of this input subunit component."

::= { finSupplyMediaInputEntry 10 }

finSupplyMediaInputVendorModel OBJECT-TYPE

SYNTAX      DisplayString(0..63)

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

"The model name of this input subunit."

::= { finSupplyMediaInputEntry 11 }

finSupplyMediaInputVersion OBJECT-TYPE

SYNTAX      DisplayString(0..63)

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

"The version string for this input subunit."

::= { finSupplyMediaInputEntry 12 }

finSupplyMediaInputSerialNumber OBJECT-TYPE

SYNTAX      DisplayString(0..63)

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

"The serial number assigned to this input subunit."

::= { finSupplyMediaInputEntry 13 }

finSupplyMediaInputDescription OBJECT-TYPE

SYNTAX      DisplayString(0..255)

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

"A free form text description of this input subunit in the

localization specified by prtGeneralCurrentLocalization."

::= { finSupplyMediaInputEntry 14 }

finSupplyMediaInputSecurity OBJECT-TYPE

SYNTAX      PresentOnOff

MAX-ACCESS  read-write

STATUS      current

DESCRIPTION

"Indicates if this subunit has some security associated

with it."

::= { finSupplyMediaInputEntry 15 }

-- Finisher Supply Media, Extended Media Input Group

--

-- This group is optional. However, to claim conformance to this

-- group it is necessary to implement every object in the group.

--

-- This group defines objects that augment the

-- finSupplyMediaInputType object for this input subunit.

--

-- The Extended Media Input Group objects support identification

-- of media installed or available for use on a finisher device.

-- Medium resources are identified by name. and include a

-- collection of characteristic attributes that may further be

-- used for selection or management of them.

finSupplyMediaInputMediaWeight OBJECT-TYPE

SYNTAX      Integer32

MAX-ACCESS  read-write

STATUS      current

DESCRIPTION

"The weight of the media associated with this Input device

in grams per meter squared.  The value (-1) means other

and specifically indicates that the device places no

restriction on this parameter.  The value (-2) means

unknown.  This object can be used to calculate the weight

of individual pages processed by the document finisher.

This value, when multiplied by the number of pages in a

finished set, can be used to calculate the weight of a set

before it is inserted into a mailing envelope."

::= { finSupplyMediaInputEntry 16 }

finSupplyMediaInputMediaThickness OBJECT-TYPE

SYNTAX      Integer32

MAX-ACCESS  read-write

STATUS      current

DESCRIPTION

"This object identifies the thickness of the input media

processed by this document input subunit measured in

micrometers.  This value may be used by devices (or

operators) to set up proper machine tolerances for the

feeder operation.  The value (-2) indicates that the media

thickness is unknown or not used in the setup for this

input subunit."

::= { finSupplyMediaInputEntry 17 }

finSupplyMediaInputMediaType OBJECT-TYPE

SYNTAX      DisplayString(0..63)

MAX-ACCESS  read-write

STATUS      current

DESCRIPTION

"The name of the type of the type of medium associated with

this input subunit.  Valid values are standardized strings

from ISO 10175 (DPA) and ISO 10180 (SPDL) which are:

stationary, transparency, envelope, envelope-plain,

envelope window, continuous-long, continuous-short,

tab-stock, labels, multi-layer."

::= { finSupplyMediaInputEntry 18 }

finSupplyMediaInputMediaFormParts OBJECT-TYPE

SYNTAX      Integer32

MAX-ACCESS  read-write

STATUS      current

DESCRIPTION

"The number of parts associated with the media associated

with this input subunit if the media is a multi-part form.

The value (-1) means other and specifically indicates the

device places no restrictions on this parameter. The value

(-2) means unknown."

::= { finSupplyMediaInputEntry 19 }

-- Finisher Device Attribute Group

--

-- A finisher device subunit may have one or more parameters that

-- cannot be specified by any other objects in the MIB.  The

-- Device Attribute group allows the definition of these

-- parameters.

finDeviceAttributeTable OBJECT-TYPE

SYNTAX     SEQUENCE OF FinDeviceAttributeEntry

MAX-ACCESS not-accessible

STATUS     current

DESCRIPTION

"The attribute table defines special parameters that are

applicable only to a minority of the finisher devices.

An attribute table entry is used, rather than unique

objects, to minimize the number of MIB objects and to

allow for expansion without the addition of MIB objects.

Each finisher device is represented by a separate row

in the device subunit attribute table."

::= { finisherMIB 21 }

finDeviceAttributeEntry OBJECT-TYPE

SYNTAX     FinDeviceAttributeEntry

MAX-ACCESS not-accessible

STATUS     current

DESCRIPTION

"Each entry defines a finisher function parameter that

cannot be represented by an object in the finisher

device subunit table."

INDEX  { hrDeviceIndex, finDeviceIndex,

finDeviceAttributeTypeIndex }

::= { finDeviceAttributeTable 1 }

FinDeviceAttributeEntry ::= SEQUENCE {

finDeviceAttributeTypeIndex        FinAttributeTypeTC,

finDeviceAttributeInstanceIndex    Integer32,

finDeviceAttributeValueAsInteger   Integer32,

finDeviceAttributeValueAsOctets    OCTET STRING

}

finDeviceAttributeTypeIndex OBJECT-TYPE

SYNTAX      FinAttributeTypeTC

MAX-ACCESS  not-accessible

STATUS      current

DESCRIPTION

"Defines the attribute type represented by this row."

::= { finDeviceAttributeEntry 1 }

finDeviceAttributeInstanceIndex OBJECT-TYPE

SYNTAX      Integer32

MAX-ACCESS  not-accessible

STATUS      current

DESCRIPTION

"An index that allows the discrimination of an attribute

instance when the same attribute occurs multiple times for

a specific instance of a finisher function.  The value of

this index shall be 1 if only a single instance of the

attribute occurs for the specific finisher function."

::= { finDeviceAttributeEntry 2 }

finDeviceAttributeValueAsInteger OBJECT-TYPE

SYNTAX      Integer32

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

"Defines the integer value of the attribute.  The value of

the attribute is represented as an integer if the

finAttributeTypeTC description for the attribute has the

tag 'INTEGER:'.

Depending upon the attribute enum definition, this object

may be either an integer, a counter, an index, or an enum.

Attributes for which the concept of an integer value is

not meaningful SHALL return a value of -1 for this

attribute."

::= { finDeviceAttributeEntry 3 }

finDeviceAttributeValueAsOctets OBJECT-TYPE

SYNTAX      OCTET STRING (SIZE(0..63))

MAX-ACCESS  read-only

STATUS      current

DESCRIPTION

"Contains the octet string value of the attribute.  The

value of the attribute is represented as a string if the

finAttributeTypeTC description for the attribute has the

tag 'OCTETS:'.

Depending upon the attribute enum definition, this object

may be either a coded character set string (text) or a

binary octet string.  Attributes for which the concept of

an octet string value is not meaningful SHALL contain a

zero length string."

::= { finDeviceAttributeEntry 4 }

END