Spec for a simple Media All In One Name

From: Tom Hastings, Bob Herriot

File: simple-all-in-one-names.doc

Date: 7/25/01

This paper proposes a very simple definition for a Media All In One Name for our Media Names Standard, as suggested by Harry and Mark.

The basic idea is to represent the separate sets of names as fields in a single string, with each field separated by a "." character.  This syntax is compatible with the IPP keyword syntax (all lower case, plus "." and "-") and can be used with the current IPP/1.1 client and Printer implementations of "media", "media-default", "media-ready", and "media-supported" attributes.

So far we have defined the following Names which would be separate fields:

Media Size Self Describing Name

Media Type Name

Media Color Name

where:

The ABNF for the Media Size Self Describing Name is:

prefix “_” size_name "_" short_dim "x" long_dim units

The Media Type Names are:

stationery           -- default

transparency

envelope

envelope-plain

envelope-window

continuous

continuous-long

continuous-short

tab-stock

pre-cut-tabs

full-cut-tabs

multi-part-form

labels

multi-layer

screen

screen-paged

photographic

cardstock

and we've agreed to add 'roll' and drop 'other'

The Media Color Names are:

no-color

white                -- default

pink

yellow

blue

green

buff

goldenrod

red

gray

ivory

orange

A valid Media All In One Name MUST include the Media Size Self Describing Name (both Size Name and Dimensions fields) followed by other fields which MUST be in the following order, but any field whose value is the indicated default value above MUST be omitted, including the "_" separator character:

# Media Type Name

# Media Color Name

Implementers MAY add additional fields.  They MUST occur after the fields defined in this standard.  Implementers MAY add additional field values to defined fields.

Note that if a given field is not supported by an implementation, omitting that field is assumed to have the meaning of the default above.  Thus this specification places no burden on implementations to support more than the Media Size Self Describing Name field in a Media All In One Name.  Also the defaulting rules make the names much shorter, more compatible with the current IPP values, and aligned with current practice.

Thus there is no burden on implementations in defining the following additional fields.  These definitions also provide a simple one-to-one mapping to the PWG IEEE-ISTO 5100.3 Production Printing Attributes - Set1 extension:

# Media Front Coating Name

# Media Back Coating Name

The Media Coating Names are:

none                 -- default

glossy

high-gloss

semi-gloss

satin

matte

# Media Preprinted Name

none                   -- default

preprinted

letterhead

# Media Hole Count Name

holes-0                -- default

holes-1

holes-2

holes-3

holes-4

holes-5

# Media Order Count Name

ordered-1              -- default

ordered-2

ordered-3

ordered-4

ordered-5

ordered-6

# Media Recycled Name

none                   -- default

recycled

We haven't come up with a satisfactory proposal for Media Weight Names, since there is no obvious default that we could define.  So we say that the default value is 'unspecified', meaning that leaving out the weight means that the weight is unspecified:

# Media Weight Name

unspecified            -- default

nnn-grams

We should also add bond as a separate field, rather than adding it to the Media Type Name, since 'bond' is relatively orthogonal to Media Type:

# Media Bond Name

none                   -- default

bond

ISSUE 01:  Is the order for all of the fields above the best for the canonical ordering?

ISSUE 02:  Should Media Bond Name field be moved up higher to be neared other more similar fields?

Examples:

na_letter_8.5x11   -- white stationery, no holes, etc.  In other words, the size name by itself is the white stationery media, as in IPP

na_personal_3.625x6.5_envelope    -- white envelope, no holes, not recycled, etc.

na_letter_8.5x11_transparency_no-color -- clear transparency

na_3x5_3x5_photographic_front-matte  -- white photographic front matte

na_3x5_3x5_cardstock_blue            -- blue 3x5 card stock

na_letter_8.5x11_blue                  -- blue stationery, no holes, etc.

na_letter_8.5x11_front-glossy          -- white glossy on front side

na_letter_8.5x11_front-glossy_back-glossy  -- white glossy both sides

na_letter_8.5x11_holes-3               -- three holed white stationery

na_letter_8.5x11_envelope_blue         -- blue envelope

na_letter_8.5x11_recycled              -- recycled white stationery

na_letter_8.5x11_envelope_blue_recycled -- recycled blue envelope

na_letter_8.5x11_bond              -- white bond stationery, no holes, etc.

na_letter_8.5x11_envelope_bond     -- white bond envelope, etc.

na_letter_8.5x11_letterhead_bond   -- white bond letterhead, etc.

na_letter_8.5x11_80-gram  -- 80 grams per square meter white stationery.  All of the examples above this one are of an unspecified weight, while this one is 80 grams per square meter weight.

na_personal_3.625x6.5_envelope_blue_front-glossy_back-glossy_recycled_letterhead_bond_80-gram -- example with all non-default values